## Slide 1: WF on Repeater Classes and Types
CMCC
3GPP TSG-RAN WG4 Meeting # 99-e R4-2108082
Electronic Meeting, May 19-27, 2021

## Slide 2: WF on repeater classes for DL (access link)
Agreement: at least 2 classes as the baseline for at least FR1
  Also introduce for FR2 if there is any differentiation in DL related requirements between the scenarios/classes. If no requirement differentiation between scenarios, no need for FR2 downlink scenarios/classes.
  Class for [Local area/Pico deployment] shall be introduced
  FFS whether [Medium/Micro] ,[wide area/Macro] and /or [Home/Femto] can be introduced
Further discuss on
  how to differentiate the 2 (or 3) classes:
    use the similar same approach as BS/IAB class definition with deployment scenario (e.g. Local Area, Medium Range, Wide Area); Further discuss the associated deployment scenario with Repeater class definition
  whether a 3rd class is also needed depending on whether FR1 (or FR2).
  Further discuss on co-existence of the proposed classes

## Slide 3: WF on repeater Classes for FR1 FDD/TDD UL (backhaul link)
Agreement: at least 2 classes as the baseline
  Class for [LA/Pico deployment] will be included
  FFS for other class(es)
  The same principle of how to define/differentiate class also apply for FR1 TDD UL
Further discuss on
  how to differentiate the 2 classes
    use the similar approach as IAB class definition with deployment scenario description (e.g. planned/unplanned with a subset of WA/MR/LA) ; Further discuss the associated deployment scenario with Repeater UL class definition
  whether a 3rd class is also needed.

## Slide 4: WF on repeater Classes for FR2 UL (backhaul link)
Agreement
    Introduce two classes, one class with maximum power limited by PC1 and the other without power limit
  Further discuss on how to define class
    Option 1: Similar approach to IAB; i.e. formal class definition (e.g. MR) with deployment scenario description (e.g. planned/unplanned); Further discuss the associated deployment scenario with Repeater UL class definition

## Slide 5: WF on relationship between repeater classes for DL and UL TX
  Agreement: UL(BS side for UL transmission ) and DL (UE side for DL transmission) classes(or what definition/differentiation will be used) are decoupled.
  Further discuss if receiver requirements also need to be differentiated.

## Slide 6: WF on repeater types
  Agreement: Introduce types 1-C and 2-O
  further discuss if 1-H or 1-O is also needed or at least try to have some decision criteria for introduction of 1-H; and make decision on the necessity of introduction of 1-H and 1-O in Rel-17 repeater WI in August RAN4 meeting