## Slide 1: WF on gNB positioning measurement requirements
Ericsson
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May 19-27, 2021
Agenda: 6.5.2.3
R4-2108314

## Slide 2: General: Beam sweeping during gNB measurement
Add following note in SRS-RSRP and gNB Rx-Tx accuracy sections: outside the accuracy tables and will not be part of the accuracy side conditions:
  Note: The measurement accuracy requirements are defined under an assumption that gNB is not mandated to perform receive beam sweeping.

## Slide 3: SRS-RSRP: SRS BW grouping for accuracy requirements
SRS BW grouping for defining SRS-RSRP accuracy requirements
  FR1
    24 ≤ BW < 48 (requirements will be defined for Ês/Iot ≥ 3dB only)
    48 ≤ BW < 132
    132 ≤ BW
  FR2
    32 ≤ BW < 64 (requirements will be defined for Ês/Iot ≥ 3dB only)
    64 ≤ BW < 132
    132 ≤ BW

## Slide 4: SRS-RSRP: Averaging method for deriving results without RF margins
SRS-RSRP average (SRS-RSRPavg) without RF margin used for baseline accuracy requirements is derived as follows:
  SRS-RSRPavg = [ceil(2*avg(CDF90(SRS-RSRP)))/2] + 0.5 dB (If std dev > 0.25 dB)

## Slide 5: SRS-RSRP: Impact of SRS Ês/Iot on accuracy
SRS-RSRP accuracy depends on SRS Ês/Iot.

## Slide 6: SRS-RSRP: Impact of SRS symbol and comb size on accuracy
SRS-RSRP accuracy will be defined agnostic to symbols and comb size according to the agreed SRS BW grouping and based on the combination of {comb=2, symbol=1}.

## Slide 7: SRS-RSRP: RF margin for SRS-RSRP accuracy for different gNB types
RF calibration margin differs between gNB type 1-C and other gNB types:
  X= [2.5] dB for gNB type 1-C
  X= [4] dB for gNB type 1-H, 1-O and 2-O

## Slide 8: gNB Tx-Tx: SRS BW grouping for accuracy requirements
SRS BW grouping for defining gNB Rx-Tx time difference accuracy requirements
  FR1
  FR2
SRS bandwidth in RB | SCS [kHz]
24 ≤ BW ≤ 40 (requirements will be defined for Ês/Iot ≥ 3dB only) | 15
44 ≤ BW ≤ 84 | 
88 ≤ BW ≤ 168 | 
176 ≤ BW | 
48 ≤ BW ≤ 84 | 30
88 ≤ BW ≤ 168 | 
176 ≤ BW | 
48 ≤ BW ≤ 84 | 60
88 ≤ BW | 
SRS bandwidth in RB | SCS [kHz]
132 ≤ BW ≤ 168 | 60
176 ≤ BW | 
32 ≤ BW ≤ 40 | 120
44 ≤ BW ≤ 84 | 
88 ≤ BW | 
The accuracy numbers can be revisited based on the new simulation results for the lower bounds of SRS BW ranges which were not simulated (i.e. 44 RBs, 88 RBs, 176 RBs).

## Slide 9: gNB Rx-Tx: Averaging method for deriving results without RF margins
gNB Rx-Tx average (gNB Rx-Tx)avg without RF margin used for baseline accuracy requirements is derived as follows:
  (gNB Rx-Tx)avg = ceil(avg(CDF90(gNB Rx-Tx)))
The above averaging method for derving the baseline gNB Rx-Tx accuracy can be revisited to take into account the spread of proposals from contributing companies.

## Slide 10: gNB Rx-Tx: Impact of SRS Ês/Iot on accuracy
gNB Rx-Tx: accuracy depends on SRS Ês/Iot.

## Slide 11: gNB Rx-Tx: Impact of SRS symbol and comb size on accuracy
gNB Rx-Tx accuracy will be defined agnostic to symbols and comb size according to the agreed SRS BW grouping and based on the combination of {comb=2, symbol=1}.