## Slide 1: WF on CSI-RS based L3 measurement requirements
CATT,…
3GPP TSG-RAN WG4 Meeting #99-e R4-2108317 Electronic Meeting, 19th – 27th May, 2021
Agreement in 1st round
Agreement in GTW (Apr. 16th)
Agreement in 2nd round

## Slide 2: Sub-topic 1-1 Time domain restriction for CSI-RS configuration
Agreement
  FR1
    For inter-frequency measurements, Rel-16 L3 CSI-RS requirements are defined under assumption that all CSI-RS resources in the same MO are configured in the same 5ms window
    For intra-frequency measurements: Rel-16 L3 CSI-RS requirements are defined under assumption that CSI-RS resources in the same MO can be configured in up to two separated 5ms windows during one CSI-RS resource period
      1/ The overlapping status with MG is same for the two windows.
        FFS how to capture this in the specification
      2/ The periodicity of the configured CSI-RS resources is 20ms or 40ms.
      3/ The gap between two 5ms windows shall be half of the CSI-RS periodicity
      4/ Measurement requirements are not impacted by separated 5ms windows.
      The conditions 1, 2, 3, 4 apply for the case of two separated 5ms windows during one CSI-RS period only.
  FFS for FR2

## Slide 3: Sub-topic 1-2 UE behavior when the timing offset exceeds the threshold with single FFT assumption
Option 1: (Nokia, Intel, Apple)
  For intra-frequency measurement, the UE is not required to report the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between serving and the corresponding neighbour cell exceeds the threshold.
  For inter-frequency measurement, UE can pick up any cell as the reference cell per frequency layer. UE is not required to report the configured CSI-RS resources of a neighbour cell if the symbol level misalignment between the reference cell and the corresponding neighbour cell belonging to the same frequency layer exceeds the threshold.
Option 2: (Huawei, CATT, OPPO, Xiaomi, Qualcomm, MTK, Intel, vivo)
  No spec updates are needed.

## Slide 4: Sub-topic 1-3 Time validity of the detected associatedSSB
Agreements:
      Adding the time validity of detected associatedSSB and SFN information in 9.10.2.5 section:
          If the associatedSSB which has been detectable at least for the time period Tidentify_intra_with_index defined in clause 9.2.5.1 becomes undetectable for a period ≤ 5 seconds and then the associatedSSB becomes detectable again with the same spatial reception parameter provided the timing to that cell has not changed more than ± 3200 Tc, PSS/SSS detection time and time period used to acquire the SFN information are equal to 0.

## Slide 5: Sub-topic 2-1 Valid condition of CSI-RS configuration in the specification
Agreements:
    The accuracy requirements in Table 10.1.2.3.2-1 are valid under the following conditions:
      The bandwidth of CSI-RS is 48 PRBs and the density is 3.
      The performance with larger bandwidth of CSI-RS is equal to or better than the accuracy requirements in Table 10.1.2.3.2-1.

## Slide 6: Sub-topic 2-2 CSI-SINR measurement accuracy requirements
Agreements in RAN4#98bis-e meeting:
  Specify CSI-SINR accuracy requirement based on the following conditions on timing offset between the reference measurement timing and the target CSI-RS (T) and Es/Iot side condition(s)
    Side condition #1:
      |TΔ|≤ CP/2 and Es/Iot ≤ 15 dB
    Side condition #2
      |TΔ|≤ CP and Es/Iot ≤ [6] dB
      Note: the value of Es/Iot can be revisited based on additional simulation results in next meeting.
      No dedicated test cases will be introduced for side condition #2
Agreements in this meeting
  Es/Iot upper bound for side condition #2 of CSI-SINR accuracy requirements is 4dB.