## Slide 1: WF on NR HST UE capabilities
CMCC
3GPP TSG-RAN WG4 Meeting # 99-e R4-2108331
Electronic Meeting, May. 19-27, 2021

## Slide 2: Background
Agreed WF in RAN4#98bis meeting (R4-2105853 WF on Rel-16 NR HST UE capabilities, CMCC):
  Add two new UE capabilities to
    10-4) Support of intra-NR HST RRM measurement with speed up to 500km/h
    10-5) Support of NR-LTE inter-RAT RRM measurement with speed up to 500km/h
    Note 1: UE can indicate support of 10-4 or 10-5 only if 10-1 is NOT supported.
    Note 2: The principle of adding the capabilities is to avoid the NBC issues

## Slide 3: Issue 1-1: Clarification on requirements of 10-1
Proposal:
  Clarify in the spec that regarding UE indicating support of 10-1 but not capable of measuring on or operating under LTE with 500km/h (e.g., NR SA UE), the UE is not required to meet the Rel-16 inter-RAT HST measurement requirements specified for CONNECTED or IDLE mode.
Agreement:
  The clarification is not needed.

## Slide 4: Issue 1-2: Clarification on the applicability of HST RRM requirements
Agreements in GTW session:
  Intra-frequency HST RRM measurement shall only applies if UE supports intra-NR HST, i.e. measurementEnhancement-r16 (10-1) or the new capability intraRAT-MeasurementEnhancement-r16 (10-4).
Proposal:
  Inter-RAT NR-LTE HST RRM measurement shall only applies if UE supports inter-RAT NR-LTE HST, i.e. measurementEnhancement-r16 (10-1) or the new capability interRAT-MeasurementEnhancement-r16 (10-5).
Agreement:
  The proposal is agreed.

## Slide 5: References
TDoc | Title | Source
R4-2109225 | Discussion on UE capabilities in Rel-16 | Intel Corporation
R4-2109226 | CR on legacy Rel-16 HST NR UE measurement requirements (R16) | Intel Corporation
R4-2110367 | On UE behavior due to separate NR HST capability and on Per BC indication of per-FR gap | Huawei, HiSilicon
R4-2110368 | CR on inter-RAT measurement in HST | Huawei, HiSilicon
R4-2111259 | Discussion on addition of UE feature on enhanced CSSF for SCell measurements outside gaps | vivo
R4-2109322 | Clarification on NR-LTE inter-RAT HST RRM measurement requirements | Apple
R4-2109323 | CR on inter-RAT HST RRM measurement requirements R16 | Apple