## Slide 1: WF on per-BC indication of per-FR measurement gap UE capabilities
Qualcomm Inc.
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May. 19-27, 2021
R4-2108332
Document for: Approval

## Slide 2: Issue 2-1 Whether to introduce per-BC indication of per-FR measurement gap UE capabilities
Option 1 (Qualcomm, Huawei)
  Keep the original per UE per-FR gap indication and add new Per BC indication for the per-FR gap capacity.
Option 2 (Intel)
  RAN4 agrees on generating a new objective of R17 standards to introduce per-BC indication of per-FR measurement gap UE capabilities, was there no consensus on introducing it in Rel-16.

## Slide 3: Background Capability of ‘independentGapConfig’ (per-FR Gap)
Definitions for parameters | Per | M | FDD-TDD DIFF | FR1-FR2 DIFF
independentGapConfig This field indicates whether the UE supports two independent measurement gap configurations for FR1 and FR2 specified in clause 9.1.2 of TS 38.133 [5]. The field also indicates whether the UE supports the FR2 inter-RAT measurement without gaps when (NG)EN-DC is not configured. | UE | No | No | No

## Slide 4: Background Capability of ‘independentGapConfig’ (per-FR Gap)
During the per-UE measurement gaps the UE:
  is not required to conduct reception/transmission from/to the corresponding E-UTRAN PCell, E-UTRAN SCell(s) and NR serving cells for E-UTRA-NR dual connectivity except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
  is not required to conduct reception/transmission from/to the corresponding NR serving cells for SA (with single carrier or CA configured) except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
  is not required to conduct reception/transmission from/to the corresponding PCell, SCell(s) and E-UTRAN serving cells for NR-E-UTRA dual connectivity except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
  is not required to conduct reception/transmission from/to the corresponding NR serving cells for NR-DC except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
During the per-FR measurement gaps the UE:
  is not required to conduct reception/transmission from/to the corresponding E-UTRAN PCell, E-UTRAN SCell(s) and NR serving cells in the corresponding frequency range for E-UTRA-NR dual connectivity except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to [7].
  is not required to conduct reception/transmission from/to the corresponding NR serving cells in the corresponding frequency range for SA (with single carrier or CA configured) except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
  is not required to conduct reception/transmission from/to the corresponding PCell, SCell(s) and E-UTRAN serving cells in the corresponding frequency range for NR-E-UTRA dual connectivity except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].
  is not required to conduct reception/transmission from/to the corresponding NR serving cells in the corresponding frequency range for NR-DC except the reception of signals used for RRM measurement(s) and the signals used for random access procedure according to TS38.321 [7].

## Slide 5: Background Summary of RRM requirements with per-FR gaps
Category | Item | Enhancement upon supporting per-FR gap
ALL DL interruptions involving FR1+FR2 BC (CA and MR-DC) | All kinds of BWP switches on single CC or on multiple CC | Interruption is only allowed in the same FR where BWP switch happens
 | All kinds of SRS carrier based switching on NR or on E-UTRAN carriers | Interruption is only allowed in the same FR with the original carrier where SRS is transmitted
 | Inter-frequency SFTD measurement causing DL interruptions | Interruption is only allowed in the same FR with the target cell
 | Interruptions at CA dedicated operations: SCell addition/release, SCell activation/deactivation, interruption upon measurement on deactivated SCCs, SCell hibernation, SCell dormancy, activating multiple DL SCells | Interruption is only allowed in the same FR of the operation that happens
 | All other operations that allows interruptions: transitions related to DRX, UL carrier reconfig, UE specific BW reconfig, UL Tx switching, autonomous gaps | Interruption is only allowed in the same FR of the operation that happens
R4-2106442

## Slide 6: Background Summary of RRM requirements with per-FR gaps
Category | Item | Enhancement upon supporting per-FR gap
Delay at activation of multiple DL SCells | Activation delay of deactivated multiple DL SCells in both CGs in NR-DC | No requirement if UE is not capable of per-FR gaps
 | Activation delay upon addition of multiple DL SCells in both CGs in NR-DC | No requirement if UE is not capable of per-FR gaps
Delay at all kinds of BWP switch on multiple CCs | Simultaneous DCI based switch | Counting only the CC number within the same FR for UE with per-FR gap capability
 | Non simultaneous DCI/RRC based switch | No requirement if UE is not capable of per-FR gaps
R4-2106442

## Slide 7: Background Summary of RRM requirements with per-FR gaps
Category | Item | Enhancement upon supporting per-FR gap
Additional delay of measurement reporting upon SRS carrier switch | Intra-frequency event triggered measurement reporting | No additional delay allowed in FR2 for capable UE
 | Inter-frequency event triggered measurement reporting | No additional delay allowed in FR2 for capable UE
 | L1-RSRP measurement reporting | No additional delay allowed in FR2 for capable UE
Autonomous gaps | Autonomous gaps at RSTD measurements | No autonomous gap is allowed in FR2 for capable UE
Other categories | Other items related to measurements and measurement gaps | More demanding requirements for UE capable of per-FR gaps
R4-2106442

## Slide 8: Background potential constraints for per UE indication of per-FR gap capability
Some companies indicate that for some UE implementation, the current per-UE based capability signaling will make the feature difficult for FR1+FR2 capable UE to support it because many different requirements associated to the feature shall be fulfilled even for the highest order of CA combination that can be supported by the UE

## Slide 9: Background Complexity of NW side or maybe also of UE side
Response
  Companies comment that it will be complicated for NW to check the capability of the BC. At the worst case, gNB could just ignore the new per-BC indication and only read the original one, then nothing changed compared to Rel-15 (either support per-FR gap in all cases or not supports it at all).
  It will not frequently happen that gNB to check whether status of supporting this per-FR gap changes. It could only happen when gNB add/release a cell, before which the capability to support the new serving CC configuration under the BC will be checked anyway.
  From UE side it is the same, for UE who do not want to make the change could just use the Rel-15 indication.
Concern
  It is unnecessary complicated to use different baseband procedures (e.g. scheduling) for different BC especially when BC is reconfigured – not efficient to completely change all the network procedures. Therefore, in our view if some UEs have implementations issues for certain BC, then such UE does not have to report per FR gap capability. The default assumption is per UE gap implementation.

## Slide 10: Background Relation to the baseband resource
Response
  This issue had been discussed at the very beginning of this discussion. It mainly results from the overloading of this per-FR gap and the more and more high order FR1+FR2 BCs. And also it is implementation specific, and this is why we have different capability indications for other requirements/features as usual instead of only allowing one particular implementation.
Concern
  per-FR and per-UE measurement gap capability is introduced to accommodate two type of implementation, discrete RFIC between FR1 and FR2 and single RFIC for both FR1 and FR2. Also, the interruption related requirements has been introduced since LTE time due to single RFIC implementation.
  Almost all per-FR gap dependent requirements are interruption related either directly (e.g. interruption requirements) or indirectly (multiple SCell activation, multiple CC BWP switching, etc.). Although the question has been raised in last couple meetings, we however still don’t think the proponent companies have clear explanation why interruption related requirements are also baseband dependent.
  Also, upon the baseband dependent issues are clarified, we also need to understand if per-BC can solve the problem, since baseband capability not only involves a specify band combination but also # of CC, aggregated BW, MIMO capability, etc.

## Slide 11: Background Requirements for SCell activation of multiple CCs
Response
  It was mentioned in 4-2110367. The explanations are as following:
  For non-simultaneous DCI/RRC based BWP switching on multiple CCs and (direct) SCell activations of multiple SCells, the per-FR gap works as conditions in another way. For instance, for non-simultaneous RRC based BWP switching on multiple CC or direct SCell activation of multiple SCells, it is assumed that the feasible scenarios is NR-DC and there is one RRC messages per CG. It is possible that the RRC message is interrupted by actions in the other CG, then the requirements only apply for UE which is capable of per-FR gap, which implies that UE is able to receive two RRC messages in two CGs independently. By having the new per-BC indication, when NW trigger the BWP switch on multiple CCs or SCell activations, the serving CC configuration is not changed, which means NW also know whether the UE is capable of per-FR gap at the very moment.
Question
  Company raised the question in the meeting that there may be problem in multiple SCell activation.

## Slide 12: Background BC for serving CC or MO
Response
  One company clarified that it was for serving CC (regardless of active or not) not the MO. It means if NW configures CC1+CC2+CC3 under BC 1 where the per-FR gap is indicated supported, the per-FR gap is supported no matter whether CC1/CC2/CC3 is activated or not or what the MO configuration is.
Question
  Whether the per-BC indication works for serving CC or MO?

## Slide 13: Proposals on Issue 2-1 Whether to introduce per-BC indication of per-FR measurement gap UE capabilities
RAN4 to choose between on or the other in RAN4#99 e-meeting.
  Option 1
    Keep the original per UE per-FR gap indication and add new Per BC indication for the per-FR gap capacity.
  Option 2
    Do not introduce per-BC indication of per-FR measurement gap UE capabilities in Rel-16. Instead, capture the following in the RRM meeting minutes:
      RAN4 has a common understanding that further enhancements to the per-FR measurement gap UE capabilities can be further studied in Rel-17 (e.g. in FeRRM WI) and is subject to RAN plenary approval and available time budget.

## Slide 14: References
TDoc | Title | Source
R4-2108968 | Discussion on Rel-16 Features | Qualcomm Incorporated
R4-2109225 | Discussion on UE capabilities in Rel-16 | Intel Corporation
R4-2110367 | On UE behavior due to separate NR HST capability and on Per BC indication of per-FR gap | Huawei, HiSilicon