## Slide 1: WF on NR Ext to 71GHz - RRM Agreements from RAN4#99-e in email thread: [99-e][233] NR_ext_to_71GHz_RRM
Qualcomm
3GPP TSG-RAN WG4 Meeting #99-e R4-2108354
Electronic Meeting: 19th – 27th May 2021
Agenda Items: 9.15.6

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: Specification structure (TS 38.133)
The specification structure and ways to capture new/updated requirements would be discussed in future meetings.
The following options may be considered during the discussion:
  For licensed operation, new or updated requirements for which there’s already a section in TS 38.133, RAN4 should update the corresponding section with the 52.6-71GHz related updates.
  For unlicensed operation, RAN4 should update the corresponding sections introduced during NR-U to add the new requirements for operation in 52.6-71GHz.
  A new section dedicated to NR in 52.6-71GHz may be introduced when a completely new item applicable to NR in 52.6-71GHz only is introduced. Relevant discussion should take place only after such items have been identified and significantly discussed.

## Slide 4: Deployment scenarios
Following options are identified during the RRM discussion on this topic
  Option 1(Vivo): RAN4 works on RRM requirements for standalone single-carrier and multi-carrier operation first
  Option 2 (Nokia): RAN4 works on RRM requirements first for
    Standalone single-carrier and multi-carrier operation and CA and DC
    DC and CA with FR1.
  Option 3 (Ericsson): RAN4 to prioritize non-standalone scenario where new band is used for SCell and PCell belongs to legacy FR2 band

## Slide 5: Overall RRM impact
Study impact on RRM requirements due to at least following aspects
  Frequency range definition of the new band
  Introduction of the new band
  Further RAN1/2 agreements

## Slide 6: Impact of higher SCS on RRM requirements
Define new RRM requirements due to higher data/SSB SCS for at least the following topics:
  Timing
    UE transmit timing
    Timing advance (TA)
  Interruptions
  Active BWP switching delay
  Measurement gaps
    Interruption time
Study impact on RRM requirements due to higher SSB SCS for at least the following topics:
  Intra-frequency measurement
  Inter-frequency measurement
Other RRM requirements, if identified are not precluded.

## Slide 7: Scaling factor for RX beam sweeping
RAN4 to study whether the changes on scaling factor for RX beam sweeping are required for this frequency range support

## Slide 8: Scheduling restrictions
The need to update the scheduling restriction/availability will be further discussed, if needed, along with the relevant RRM requirements.

## Slide 9: Operation in licensed/unlicensed band
RAN4 to initially focus on RRM requirements for both licensed and unlicensed bands without considering LBT and start working on LBT impact on RRM requirements in unlicensed band based on more conclusions from RAN1.