## Slide 1: WF on RedCap RRM requirements All agreements in RAN4#99-e in email thread: [99-e][236] NR_redcap_RRM
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #99-e R4-2108359
Electronic Meeting: 19th – 27th May 2021
Agenda Items: 9.19.2

## Slide 2: RRM work plan for RedCap
RAN4 to start discussing the eDRX for IDLE/INACTIVE state from RAN4#100e meeting.
RAN4 to start discussing RRM relaxation work based on the outcome from RAN2 from RAN4#100e meeting.

## Slide 3: Specification structure and impact
RedCap specific requirements are introduced in new subsections in TS 38.133.The new sections are FFS and will be decided based on the impacted requirements as identified in issue 4-1-1.
For 36.133: RedCap specific inter-RAT requirements, if introduced, will be in new subsections in TS 36.133. The new sections are FFS and will be decided based on the impacted requirements as identified in issue 4-2-1.
RedCap requirements are developed with NR release 15 RRM requirements as baseline. Which release 16 features to be considered for RedCap are discussed in case by case manner after sufficient progress is made in the WI.

## Slide 4: Scope of RedCap in release 17
RRM requirements are developed for all three duplex modes, i.e. FD-FDD, HD-FDD type A and TDD in Release 17 RedCap.
RRM requirements are developed for both 1 Rx and 2Rx for each duplex mode (FD-FDD, HD-FDD type A and TDD).
RAN4 should focus on RRM requirements that are relevant to PCell operation, i.e. no DC or CA is considered for RedCap in release 17.
Inter-frequency mobility
  FFS whether to define inter-frequency RRM requirements for RedCap UE in Rel-17.
Inter-RAT mobility
  Option 1:
    Do not define inter-RAT RRM requirements for RedCap UE in Rel-17.
  Option 2:
    Do not define inter-RAT RRM requirements on 2G/3G for RedCap UE in Rel-17
    FFS: whether define inter-RAT RRM requirements on LTE for RedCap UE in Rel-17

## Slide 5: RRM impact on TS 38.133
Section | Type of requirements | Is requirement impacted?
3. Definitions, symbols and abbreviations | 3.1 Definitions, 3.2 Symbols, 3.3 Abbreviations | YES
 | 3.5 Frequency bands grouping | YES
 | 3.6 Applicability of requirements in this specification version | YES
4. IDLE state mobility | 4.2.2.1 UE measurement capability | YES
 | 4.2.2.2 Measurement and evaluation of serving cell | YES
 | 4.2.2.3 Measurements of intra-frequency NR cells | YES
 | 4.2.2.4 Measurements of inter-frequency NR cells | YES if inter-frequency measurements are supported
 | 4.2.2.5 Measurements of inter-RAT E-UTRAN cells | Yes if inter-RAT measurements are supported
 | 4.2.2.6 Maximum interruption in paging reception | FFS

## Slide 6: RRM impact on TS 38.133
Section | Type of requirements | Is requirement impacted?
5. INACTIVE state mobility | 5.1.2.1 UE measurement capability | Same as in IDLE
 | 5.1.2.2 Measurement and evaluation of serving cell | Same as in IDLE
 | 5.1.2.3 Measurements of intra-frequency NR cells | Same as in IDLE
 | 5.1.2.4 Measurements of inter-frequency NR cells | Same as in IDLE
 | 5.1.2.5 Measurements of inter-RAT E-UTRAN cells | Same as in IDLE
 | 5.1.2.6 Maximum interruption in paging reception | Same as in IDLE
6. CONNECTED state mobility | 6.1 Handover | FFS
 | 6.2.1 RRC re-establishment | FFS
 | 6.2.2 Random Access | FFS
 | 6.2.3 RRC Connection Release with Redirection | FFS

## Slide 7: RRM impact on TS 38.133
Section | Type of requirements | Is requirement impacted?
7. Timing | 7.1 UE transmit timing | FFS
 | 7.2 UE timer accuracy | NO
 | 7.3 Timing Advance | FFS
 | 7.4 Cell phase synchronization accuracy | NO
 | 7.5 Maximum Transmission Timing Difference | NO
 | 7.6 Maximum Receive Timing Difference | NO
 | 7.7 deriveSSB-IndexFromCell tolerance | FFS
8. Signalling characteristics | 8.1 Radio Link Monitoring | FFS
 | 8.2 Interruption | FFS
 | 8.3 SCell Activation and Deactivation Delay | Not applicalbe for Redcap in release 17
 | 8.4 UE UL carrier RRC reconfiguration delay | FFS
 | 8.5 Link Recovery Procedures | FFS
 | 8.6 Active BWP switch delay | FFS
 | 8.8 NE-DC: E-UTRAN PSCell Addition and Release Delay | Not applicalbe for Redcap in release 17
 | 8.9 NR-DC: PSCell Addition and Release Delay | Not applicalbe for Redcap in release 17
 | 8.10 Active TCI state switching delay | FFS
 | 8.11 PSCell Change | Not applicalbe for Redcap in release 17
 | 8.12 Uplink spatial relation switch delay | FFS
 | 8.13 UE-specific CBW change | FFS

## Slide 8: RRM impact on TS 38.133
Section | Type of requirements | Is requirement impacted?
9. Measurement Procedure | 9.1 General measurement requirement | YES
 | 9.2 NR intra-frequency measurements | YES
 | 9.3 NR inter-frequency measurements | YES if inter-frequency measurements are supported
 | 9.4 Inter-RAT measurements | Yes if inter-RAT measurements are supported
 | 9.5 L1-RSRP measurements for Reporting | FFS
 | 9.6 NE-DC: Measurements | Not applicalbe for Redcap in release 17
 | 9.7 Cross Link Interference measurements | FFS
 | 9.8 L1-SINR measurements for Reporting | FFS
 | 9.9 NR measurements for positioning | FFS
 | 9.10 CSI-RS based L3 measurements | FFS
 | 9.11 NR measurements with autonomous gaps | FFS
10. Measurement Performance requirements | 10.1 NR measurements | YES
12. V2X Requirements | V2X Requirements | FFS

## Slide 9: RRM impact on TS 36.133
Section | Type of requirements | Is requirement impacted?
3. Definitions, symbols and abbreviations | 3.1 Definitions, 3.2 Symbols, 3.3 Abbreviations | YES if inter-RAT measurements are supported
4. E-UTRAN RRC_IDLE state mobility | 4.1 Cell Selection | FFS
 | 4.2 Cell Re-selection | YES if inter-RAT measurements are supported
 | 4.3 Minimization of Drive Tests (MDT) | N/A
 | 4.4 MBSFN Measurements | N/A
 | 4.5 Proximity-based Services | N/A
 | 4.6 Cell Selection and Re-selection Requirements for UE category NB1 | FFS
 | 4.7 Cell Selection and Re-selection Requirements for UE category M1 | FFS
 | 4.8 Idle State Positioning Measurement Requirements for UE category NB1 | N/A
5. E-UTRAN RRC_CONNECTED state mobility | 5.1 E-UTRAN Handover | N/A
 | 5.3 Handover to other RATs | YES if inter-RAT measurements are supported
 | 5.4 Handover to Non-3GPP RATs | N/A
 | 5.5 E-UTRAN Handover for Cat-M1 UEs | FFS
 | 5.7 E-UTRAN DAPS Handover | N/A

## Slide 10: RRM impact on TS 36.133
Section | Type of requirements | Is requirement impacted?
6. RRC Connection Mobility Control | 6.1 RRC Re-establishment | N/A
 | 6.2 Random Access | N/A
 | 6.3 RRC Connection Release with Redirection | FFS
 | 6.4 CSG Proximity Indication for E-UTRAN and UTRAN | N/A
 | 6.5 RRC Re-establishment for NB-IoT UEs | N/A
 | 6.6 Random Access for UE category NB1 | N/A
 | 6.7 RRC Re-establishment for Cat-M1 UEs | N/A
 | 6.8 RRC Connection Release with Redirection for Cat-M1 UEs | FFS
 | 6.9 RRC Connection Redirection to Non-anchor Carrier in NB-IoT | FFS
7. Timing and signalling characteristics |  | N/A
8. UE Measurements Procedures in RRC_CONNECTED State |  | N/A
9. Measurements performance requirements for UE |  | N/A
10. Measurements Performance Requirements for E-UTRAN |  | YES if inter-RAT measurements are supported
11. ProSe Requirements in Any Cell Selection state |  | N/A
12. V2V Sidelink Communication Requirements for V2V Operation on Dedicated V2V Carrier |  | N/A
13. V2X Requirements |  | N/A