## Slide 1: WF on R17 further Multi-RAT Dual-Connectivity enhancements
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #99
Electronic Meeting, May. 19-27, 2021
      R4-2108363
Document for: Approval

## Slide 2: Work Plan
According to WID [RP-201040], core part aims to be finalized by March 2022, performance part aims to be finalized by September 2022
  RAN4#99-e
    Discuss and approve the work plan for RRM part.
    Discuss and identify which RRM requirements need to be specified for
      Conditional PSCell change and addition
      Efficient activation/de-activation mechanism for one SCG
      Efficient activation/de-activation mechanism for SCells in NR CA
    Reply RAN1/2 LS, if any
  RAN4#100-e
    Discuss the identified RRM requirements on
      Conditional PSCell change and addition
      Efficient activation/de-activation mechanism for one SCG
      Efficient activation/de-activation mechanism for SCells in NR CA
    Reply RAN1/2 LS, if any
  RAN4#100-e-bis
    Continue to discuss the identified RRM requirements on
      Conditional PSCell change and addition
      Efficient activation/de-activation mechanism for one SCG
      Efficient activation/de-activation mechanism for SCells in NR CA
    Provide draft CR on TS38.133
    Reply RAN1/2 LS, if any

## Slide 3: Work Plan
According to WID [RP-201040], core part aims to be finalized by March 2022, performance part aims to be finalized by September 2022
  RAN4#101-e
    Further discuss the RRM requirements on
      Conditional PSCell change and addition
      Efficient activation/de-activation mechanism for one SCG
      Efficient activation/de-activation mechanism for SCells in NR CA
    Provide and refine the draft CR
  RAN4#102-e
    Approve the CRs on TS38.133
  RAN4#102-e-Bis (RRM performance part only)
    Discuss and decide test case list and related parameters
  RAN4#103-e (RRM performance part only)
    Provide draft test cases for RRM
  RAN4#104-e (RRM performance part only)
    Approve test cases for RRM

## Slide 4: Temporary RS for efficient SCell activation
SCell being activated is known and belongs to FR1
  If SCell measurement cycle is larger than 160ms, the minimum gap length between the RS symbol(s) for AGC and the RS symbols for time/frequency acquisition is
      -Option 1: 2 slots
      -Option 2: 2ms
  If SCell measurement cycle is larger than 160ms, whether the UE requires to receive another RS transmitted also on the other activated serving cell in the same band in the same slot?
      -Option 1: These RSs are not required to be transmitted in the same slot
      -Option 2: These RSs are required to be transmitted in the same slot
      -Option 3: UE reports capability which indicates whether UE requires to receive another RS transmitted also on the other activated serving cell in the same band in the same slot.

## Slide 5: Temporary RS for efficient SCell activation
SCell being activated is unknown and belongs to FR1
  when SCell is non-contiguous to an active serving cell in the same band (Intra-band non-continuous CA), or when Scell to be activated and active serving cell are in the different band (Inter-band CA), whether temporary RS can be used for AGC and/or time frequency tracking?
    It is not a target scenario for temporary RS based SCell activation latency optimization.
    The agreement above applies based on RAN1 working assumptions on temporary RS design provided in the LS R1-2009798.

## Slide 6: Temporary RS for efficient SCell activation
SCell being activated belongs to FR2
  If there is no active serving cell on that FR2 band and the Scell being activated is unknown to UE,
    It is not a target scenario for temporary RS based SCell activation latency optimization.
    The agreement above applies based on RAN1 working assumptions on temporary RS design provided in the LS R1-2009798.

## Slide 7: Temporary RS for efficient SCell activation
Certain TDD configurations
  For all kinds of AGC or T&F tracking operations, two slots of temporary RS resources are needed to facilitate fair performance (Moderator added for further clarification: even for some TDD configurations where no two consecutive slots are indicated as downlink slots.)

## Slide 8: Temporary RS for efficient SCell activation
New incoming LS [R4-2107609]
  Whether or not RAN4 specify requirements for Option 2
    Option 1(Ericsson, vivo, Intel, Huawei, ZTE, OPPO, Nokia, MTK, vivo, Apple): Do not support option 2 but simply go with option 1a (indicated in LS).
    Option 2 (Qualcomm): RAN4 to determine whether or not to define requirements for additional SCell activation latency reduction based on legacy Rel-15/16 UL DCI triggering A-TRS for to-be-activated SCell. If introduced, the following should be discussed and specified in detail:
      -Corresponding SCell activation sequence
      -Applicable scenarios, e.g. whether to consider unknown SCell activation for the enhancement
      -When and on which carrier UE can expect the DCI
      -UE behavior if all or some of the DCI are not detected during the SCell activation procedure
1. Overall Description: With respect to efficient SCell activation for NR CA, RAN1 would like to inform RAN4 the following RAN1 agreement, Agreement For efficient activation of SCells Option 1a: MAC CE(s) contained in a single PDSCH to trigger both SCell activation and corresponding temporary RS(s) Details FFS including timeline design for receiving temporary RS Note: Separate from the support of Option 1a, it is up to RAN4 whether or not to consider an activation time enhancement for Option 2 without requiring further RAN1 work Option 2: A Rel-15/16 SCell activation MAC-CE to trigger SCell activation and a Rel-15/16 DCI to trigger corresponding Rel-15/16 A-TRS(s)

## Slide 9: Efficient activation/de-activation mechanism for one SCG
RAN4 are to discuss the potential RRM impacts due to efficient activation/de-activation mechanism for one SCG
  L3 RRM measurement on PSCell after SCG deactivation (Issue 3-1-1)
    what RRM measurements are needed for UE maintaining downlink synchronization to allow a quick transition from deactivated to active SCG state
    FFS: reporting requirements for deactivated PSCell
    FFS: measurement accuracy requirements for deactivated SCG
  The requirements of SCG activation/deactivation delay requirements (Issue 3-1-3)
  The requirements for RLM/BFD/BFR/beam management on deactivated PSCell, if RAN2 decides to do so (Issue 3-1-6)
  Any interruption requirements related to activation/deactivation of SCG (Issue 3-1-7)
  FFS: whether existing MCG measurement requirements apply for the MCG when the SCG is deactivated (Issue 3-1-2)
  FFS: Requirement for SCG deactivation delay requirement when one or more Scells in SCG are active or dormant (Issue 3-1-4)
  FFS: Additionally define minimum delay requirements for direct activation of SCG (Issue 3-1-5)
  FFS: Reduced physical layer processing delay for SCG activation use case (Issue 3-1-8)

## Slide 10: Conditional PSCell change and addition
Inter-SN conditional PSCell change requirements
  Option 1: The inter-SN conditional PSCell change requirements can reuse the existing conditional PSCell change requirements specified in clause 8.11B.
  Option 1 can be as a starting point
RAN4 need to define conditional PSCell addition delay
FFS: Develop related requirements for: FR1-FR1, FR1-FR2, FR2-FR1 and FR2-FR2
Deprioritize the discussion on the RRM requirements of coexistence of CHO and CPAC, until RAN2 has completed the concrete solutions.