## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e Electronic Meeting, May 19th – 27th, 2021
Huawei, HiSilicon
Way forward on NR-U BS demodulation requirements
R4-2108515

## Slide 2: Background
R4-2012611, Way Forward on NR-U BS demodulation requirements, Ericsson, RAN4#96-e
R4-2017688, Way forward on NR-U BS demodulation requirements for general part and PUSCH, Huawei, HiSilicon, RAN4#97-e
R4-2017467, Way forward on PUCCH demodulation requirements, Ericsson , RAN4#97-e
R4-2017468, Way forward on PRACH demodulation requirements, Nokia , RAN4#97-e
R4-2103988, Way forward on NR-U BS demodulation requirements for general part and PUSCH, Huawei, HiSilicon, RAN4#98-e
R4-2103989, Way Forward on NR-U PUCCH demodulation requirements, Ericsson, RAN4#98-e
R4-2103808, Way forward on NR-U PRACH demodulation requirements, Nokia, RAN4#98-e
R4-2106010, Way forward on NR-U BS demodulation requirements, Huawei, HiSilicon, RAN4#98-bis-e

## Slide 3: Performance requirements
The simulation results are summarized in R4-2110507.
The agreed rules for derivation of performance requirements for NR Rel-15 in R4-1904713 are reused and implemented in the summary of R4-2110507
SNR values in column ”38.104 Req” and ”38.141 Req” in summary R4-2110507 will be used as the performance requirements and captured in the corresponding CRs with square bracket in this meeting. Company can further check and update their results for next RAN4#100-e meeting.
Exception to PUCCH format 3:
  The averaged impairment results in column “AVE” will be used as the performance requirements and captured in the corresponding CRs with square bracket in this meeting
  Company is encouraged to double check and update the related results if possible for next RAN4#100-e meeting
  If still larger span exist among companies’ results, certain way forward should be figured out in next RAN4 meeting

## Slide 4: CG-UCI requirements
  Background：Agreement made during RAN4#98-bis-e
    Pattern of CG-UCI information bits
    Use a bit pattern {c0,c1,…,c17} that consists of :
      HARQ process number: [c0,c1,c2,c3] = [0 0 0 1]
      RV sequence: [c4,c5] = [0 0]
      NDI: [c6]
        Option 1: [c6] = [1]
        Option 2: [c6] = toggle for every new transmission, e.g. 0 for even transmissions and 1 for odd ones
      COT sharing information field: [c7,c8,…c17] = [0,0,0,0,0,0,0,0,0,0,0]
NDI: [c6] = [1]
FRC:
  Further updates are needed as per the way forward R4-2108503 in next meeting

## Slide 5
Parameter |  | Value
Channel model |  | TDLA30-10
Bandwidth |  | 20MHz
Transform precoding |  | Disabled
Antenna configuration |  | 1T2R Low
Default TDD UL-DL pattern |  | 30 kHz SCS:7D1S2U, S=6D:4G:4U 15 kHz SCS: 3D1S1U S=10D:2G:2U
MCS |  | MCS 20
HARQ | Maximum number of HARQ transmissions | 1
 | RV sequence | 0
DMRS | DM-RS configuration type | 1
 | DM-RS duration | Single-symbol DM-RS
 | Additional DM-RS position | pos1
 | Number of DM-RS CDM group(s) without data | 2
 | Ratio of PUSCH EPRE to DM-RS EPRE | -3 dB
 | DM-RS port(s) | {0}
 | DM-RS sequence generation | NID0=0, nSCID=0
Time domain resource assignment | PUSCH mapping type | A, B
 | Start symbol | 0
 | Allocation length | 14
Frequency domain resource assignment | RB assignment | 1 interlace
 | Frequency hopping | Disabled
Code block group based PUSCH transmission |  | Disabled
Test metric |  | SNR@1% BLER of CG-UCI
UCI | Number CG-UCI information bits | 18
 | Scaling | 1
 | betaOffsetCG-UCI index | 8
 | UCI partition for frequency hopping | Disabled
Simulation assumptions for CG-UCI (informative)

## Slide 6: PUCCH requirements
  Background: Agreement made during RAN4#98-bis-e
    Test metric for PF3
    Prob(DTX->ACK)<=1% and Prob(ACK miss)<=1%
    Pattern of information bits
    PF0: [0] including HARQ-ACK information only
    PF1:[0 1] including HARQ-ACK information only
    PF3: [0 0 0 0] including HARQ-ACK information only
    Pattern of PF2 information bits
    Random information bits selection
  Pattern of information bits
  PF0: [1] including ACK information only
  PF1:[0 1] including both ACK and NACK information
  PF3: [1 1 1 1] including ACK information only

## Slide 7: Simulation assumptions for PUCCH format 3 (informative)
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | 4
The number of UCI information bits | 4 bits
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | TDLA30-10 Low
Index of OCC | Not configure
Length of OCC | Not configure
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. | 
Parameter | Test 1
Modulation order | QPSK
Intra-slot frequency hopping | N/A
Group and sequence hopping | neither
Hopping ID | 0
Additional DM-RS configuration | No additional DM-RS
Number of symbols | 4
The number of UCI information bits | 4 bits
Channel bandwidth | 20MHz
SCS | 15kHz and 30kHz
Antenna configuration | 1T2R
Number of interlaces | 1
Interlace index | 0Note 1
Propagation conditions | TDLA30-10 Low
Index of OCC | Not configure
Length of OCC | Not configure
Cyclic shift index for DMRS | 0
Test metric | 
Note 1: RBs 0, 10, 20,…,90 are allocated for 15kHz and RBs 0,5,10,…,45 are allocated for 30kHz. Note 2: The UCI information does not contain CSI part 2. |