## Slide 1: WF on Rel-16 NR IAB demodulation requirements
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May. 19-27, 2021
Agenda: 6.3.6
R4-2108589
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
The following WFs were approved previously
  R4-2012644, WF on Rel-16 NR IAB demodulation requirements, RAN4#96-e.
  R4-2017673, WF on Rel-16 NR IAB demodulation requirements, RAN4#97-e.
  R4-2103994, WF on Rel-16 NR IAB demodulation requirements, RAN4#98-e.
  R4-2106172, WF on Rel-16 NR IAB demodulation requirements, RAN4#98-bis-e.
Corresponding Email summary in RAN4#98-bis-e
  R4-2108684, Email discussion summary for [99-e][325] NR_IAB_Demod.

## Slide 3: General
Test specification specific issues
  RF channels to test
    Test only the M RF channel.
  Directions for radiated testing
    For radiated requirements, test only in the OTA REFSENS receiver target reference direction.

## Slide 4: General
Editorial issues
  IAB type
    Use types following both the forms “IAB type 1-H/1-O/2-O” and “IAB-DU/MT type 1-H/1-O/2-O”, where appropriate.
  General sections in IAB-MT and IAB-DU parts
    Create separate “general” sections for IAB-DU demodulation performance requirements, IAB-MT demodulation performance requirements, and IAB-MT CSI reporting requirements. The general section contains applicability rules for each.

## Slide 5: General
Editorial issues
  Removal of parameters that are unused or left up to implementation
    Remove parameters that
      Are not configured, such as timeRestrictionForChannelMeasurements, timeRestrictionForInterferenceMeasurements, etc.
      Are related to aperiodic, such as aperiodicTriggeringOffset, reportTriggerSize, etc.
      Are related to reporting details, such as CQI/RI/PMI delay etc.
  Section to use for PMI FRC
    A.3.5.
  Notes in FRCs for CSI reporting
    Since the PBCH is left to implementation, change note2 and note3 to “PDSCH is only scheduled on slots which are full DL”.

## Slide 6: IAB-MT
CSI reporting requirements
  Test configuration for PMI and RI reporting requirements
    Adopt all PMI and RI requirements from 38.101-4, but change the reporting configuration and CSI-RS resource type to periodic, where needed, and define only NZP CSI-RS for CSI acquisition configuration in PMI and RI reporting test parameters.
  TDD pattern independence and test differentiation in PMI reporting requirements
    Keep only one radiated test (e.g., test 1) for IAB-MT PMI reporting.
  Test configuration for CQI reporting requirements
    Define only NZP CSI-RS for CSI acquisition configuration in CQI reporting test parameters.
  Test setup for CSI reporting
    Option 1: Using the following test setup for CSI reporting for IAB-MT
    Option 2: Do not introduce a new scheme for CSI reporting for IAB-MT, i.e., use the same scheme as for demodulation performance (including IAB-MT and IAB-DU) also for CSI reporting.
      Keep only one feedback link on the scheme, but add text or note that the feedback is used for CSI (only for PMI and RI reporting).
      Add a synchronization source
      Use "termination" for unused transceiver array boundary connectors.
    Option 3: Other options not precluded.
    Moderator note: Figures are also directly
    discussed in CRs.

## Slide 7: IAB - MT
Remaining issues
  General applicability rules
    IAB MT declaration for mandatory feature should be aligned with IAB-MT feature list specified in RAN2 capability signalling. Transform previous agreement to ensure PMI, RI test is optional. Previous agreements made in RAN4 still valid, if any confliction identified with IAB-MT feature list, RAN4 can further discuss in a case by case manner.
    FFS: Exact wording for conformance specifications.
  Test tolerance and measurement uncertainty selection
    Using option 2(*) from UE side as starting point, with [] into specification; companies especially TE vendors are encouraged to bring further analysis for MU/TT and RAN4 can revise the values if needed in future RAN4 meeting. Option 2(*): Reuse test tolerance values from TS 38.521-4 for IAB-MT testing.
  Test applicability with respect to capabilities/features
    Testing of RI and PMI reporting requirements specified in RAN4 for IAB-MT is declaration based, as an exceptional case.
    FFS: Usage of UE capability signalling or manufacturer declaration as configuration method concerning “applicability of requirements for mandatory IAB-MT features with capability signalling” and “applicability of requirements for optional IAB-MT features”.