## Slide 1: WF on CRS interference handling in scenarios with overlapping spectrum for LTE and NR
3GPP TSG-RAN WG4 Meeting #99e
Online Meeting, 19 May - 27 May, 2021
Agenda: 9.11.2.3
R4-2108662
China Telecom

## Slide 2: General issues

## Slide 3: General issues
  Scenarios
  According to WID, both scenarios are valid.
    Scenario 1: LTE and NR DSS
    Scenario 2: NR and LTE deployed in neighbouring BS/areas
  Scenario 1 and scenario 2 will be included for initial LLS evaluation:
    Scenario 1 with 15kHz
    Scenario 2 with 15kHz
  30 kHz for scenario 2 can be deprioritized before RAN#93e

## Slide 4: General issues
  Baseline RM scheme for performance comparison with PDSCH CRS-IM
  For scenario 1 with LTE and NR DSS:
    Rel-15 serving cell CRS-RM
    Rel-16 CRS-RM for 1 interference cell
      Case A: the 1 interference cell with RM is always the first dominant interference, i.e., INR1
      Case B: the 1 interference cell with RM is NOT always the first dominant interference. Interested companies can provide simulation results for Case B.
        e.g., INR of the 1 interference cell with RM is INR1 or INR2 with 50%: 50% probability. If the INR for the interference cell with RM is INR1, then the INR for the other interference cell is INR2, and vice versa. The INR levels for the two interference cells can be changed per [1000] slots.
        The above example for Case B is optional, and other options for Case B are not precluded.
        Case B is for initial simulation only, and FFS whether to consider it for performance requirement definition.
    Rel-15 RB symbol level RM for 2 interference cells
  For scenario 2
    No RM
    Rel-15 CRS-RM for 1 interference cell
      Case A: the 1 interference cell with RM is always the first dominant interference, i.e., INR1
      Case B: the 1 interference cell with RM is NOT always the first dominant interference. Interested companies can provide simulation results for Case B.
        e.g., INR of the 1 interference cell with RM is INR 1 or INR2 with 50%: 50% probability. If the INR for the interference cell with RM is INR1, then the INR for the other interference cell is INR2, and vice versa. The INR levels for the two interference cells can be changed per [1000] slots.
        The above example for Case B is optional, and other options for Case B are not precluded.
        Case B is for initial simulation only, and FFS whether to consider it for performance requirement definition.
    Rel-16 CRS-RM for 2 interference cells
  Companies are encouraged to bring analysis on the performance impact on LTE cell due to Rel-16 RM

## Slide 5: General issues
  Sync or async scenario for FDD
  Focus on Sync network before RP #93 meeting
  CBW and SCS for target and interference cells
  Use the following SCS/CBW for performance evaluation before RP #93e, FFS for performance requirement definition:
    FDD 15kHz: 10MHz CBW
    TDD 15kHz: to be discussed in the next meeting
    TDD 30kHz: to be discussed after RAN#93e
  PDCCH CRS-IM
  FFS whether to define neighboring cell LTE CRS-IM requirement for PDCCH

## Slide 6: Reference receiver

## Slide 7: Reference receiver
  Reference receiver
  Assume neighbouring cell CRS-IM is used together with MMSE-IRC
  Assumption on CRS-IM
  Both CRS-IC and LLR weighting for the initial performance evaluation
  FFS for performance requirements definition.
  FFS NW assistant information existed or not, companies are encouraged to bring analysis with different options.
  Number of CRS cells to be mitigated
  It’s up to UE implementation: 1 or 2 cell can be mitigated.
  UE processing time
  Encourage further analysis on UE processing time in RAN4 #100e for CRS-IC and LLR deweighting respectively.
  FFT processing
  Single FFT processing for sync scenarios.
  Further discuss for async scenarios after RAN#93e.

## Slide 8: Reference receiver (for information)
Possible implementation for CSI-IC and LLR weigthing
  CRS-IC: CRS-based channel estimation, reconstruction of CRS receive signal and substruction of this signal.
  LLR weighting: Estimation of CRS interference power level and update of LLRs for REs with CRS interference.

## Slide 9: Interference model

## Slide 10: Interference model
  Number of interfering cells modelled in the simulation
  2 interference cell will be modelled for initial LLS evaluation
  FFS for the configuration of requirements if introduced in later phase with the consideration together with the availability of NW assistant signalling.
  Interference power modeling
  Reuse the interference power modeling for LTE CRS-IM receiver, i.e., INR-i (signal level of the i-th dominant interference over Noc) methodology
  Interference power level
  Use option 1 with INR1 = 10.45 dB and INR2 = 4.6 dB as baseline, other power levels can also be simulated by interested companies.

## Slide 11: Interference model
  CRS pattern
  Non-colliding between the serving cell CRS (if exits) and interference cell CRS
  Non-colliding CRS between the two interfering cells
  For example:
    For scenario 1, v-shift = 0, 1, 2 for the serving and two interference cells
    For scenario 2, v-shift = 1, 2 for the two interference cells
PDSCH loading level on interference cell
  In time domain, probability of occurrence of data transmission in interference cells: simulate 20%, and it is also encouraged to simulate 0%, 50% and 100%.
  In frequency domain: full bandwidth allocation.

## Slide 12: Interference model
Time offset and frequency shift for sync network
  Option 1 for initial simulation:
    Time offset: The serving cell is 3 us and -1 us for interfering cell 1 and cell 2 respectively
    Frequency shift: The serving cell is 300 Hz and -100 Hz for interfering cell 1 and cell 2 respectively.
  Other options are not precluded.
Transmission rank
  Reuse the assumption from LTE HomNet CRS-IM, i.e., 80% and 20% probability for rank 1 and rank 2 transmission in the interfering cell(s).
  NR PDSCH or LTE PDSCH transmission in interfering cells
  LTE PDSCH

## Slide 13: Interference model
  Modulation scheme for the interference PDSCH
  Reuse the assumption from LTE HomNet CRS-IM, i.e., 16 QAM randomly modulated symbols in the interfering PDSCH when exists
  Precoding scheme for the interference PDSCH
  Random precoding
  MBSFN configuration for the interference LTE cell
  No MBSFN is configured on LTE carrier
Center frequency for the interference LTE cell
  Same between serving cell and neighbouring cells

## Slide 14: Target NR PDSCH parameters

## Slide 15: Target NR PDSCH parameters
  Rank for target NR PDSCH
  Rank 1
  MCS for target NR PDSCH
  Cover QPSK MCS 4 and 16QAM MCS 13 for initial simulation
  FFS whether to cover 64QAM MCS 19
  Precoding model for target NR PDSCH
  Random precoding (Single panel Type 1) with PRB bundling size is 2 with PRB bundling type is static
  HARQ process number for target NR PDSCH
  4 for FDD, further discuss for TDD
  PDSCH mapping type and DMRS configuration for target NR PDSCH
  PDSCH mapping type A with full PRB allocation, use DMRS Type 1 with single symbol front loaded and 1 additional DMRS, with FDM applied between DMRS and data.

## Slide 16: Target NR PDSCH parameters
ZP CSI-RS, NZP CSI-RS and TRS configuration for target cell
  Reuse the Rel-15 assumptions for ZP CSI-RS, NZP CSI-RS and TRS configuration in PDSCH demodulation requirements for the serving cell
  SSB position for target cell
  Configure the first SSB in slot #0 in every 20 ms, and the slot #0 in every 20 ms is not scheduled for PDSCH transmission
  Start symbol (S) and symbol length (L) for the target PDSCH
  For the scenario that Rel-15 or Rel-16 CRS-RM is configured (for scenario 1 and 2): Focus on S = 3, L = 9. Interested companies can bring analysis for S = 3, L = 11.
  For the scenario that CRS-RM is not configured (for scenario 2): S = 2, L = 12

## Slide 17: Target NR PDSCH parameters
  Overhead for TBS determination for the target PDSCH
  For the scenario that Rel-15 or Rel-16 CRS-RM is configured (for scenario 1 and 2): 18
  For the scenario that CRS-RM is not configured (for scenario 2): 0
  Target PDSCH performance measurement point
  Companies to provide simulation curves as well as the CRS-IM gain in terms of both SNR improvement and relative throughput improvement.
    Use SNR in the simulation.

## Slide 18: Common parameters for target and interfering cells

## Slide 19: Common parameters for target and interfering cells
  NR Carrier number
  Focus on NR single carrier scenario
  Tx antenna and LTE CRS port number
  For initial simulation, prioritize 4 CRS ports and interested companies can provide results for 2 CRS ports case.
  FFS for performance requirement definition.
  Rx antenna number
  2Rx and 4Rx
  Propagation condition
  TDLA30-10 and ULA low for the initial simulation

## Slide 20: Others

## Slide 21: Other aspects for RAN4 #100e
  Discuss if there is any potential impact to other WGs.
  Collection of simulation results before RAN4 #100e
  Simulation results will be collected and calibrated in RAN4 draft reflector from Aug 2nd to 5th. Interested companies are encouraged to provide simulation results before the meeting if possible.
  Template for simulation result collection is provided in R4-2108663.

## Slide 22
Thanks!