## Slide 1: WF on CQI reporting requirements for inter-cell interference MMSE-IRC
Ericsson
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
Agenda item: 9.11.2.1
Document for: Approval
R4-2108665

## Slide 2: General
Issue 1: Whether to define CQI reporting requirements with inter-cell interference scenario?
  Option 1: Yes
  Option 2: Need further discussion
  Option 3: No
  Issue 2: Whether to define PMI reporting requirements with inter-cell interference scenario?
  Option 1: Yes
  Option 2: Need further discussion
  Option 3: No

## Slide 3: Interference Model
Interference Profile
  As the starting point, model one inter-cell interferer with DIP of -0.41dB. Interferer is with static channel and target UE is with fading channel.
Interference covariance estimation granularity for CQI reporting
  Up to UE implementation
    Companies will further check the results and whether per PRB bundle size or per PRB and per slot can be considered as options for simulation alignment, if the results aren’t aligned among companies.

## Slide 4: Interference Model
Interference signal with serving cell’s NZP CSI-RS and CSI-IM REs
CSI-IM on target cell
  Option 1: Overlaps with PDSCH from interference
  Option 2: Overlaps with NZP CSI-RS from interference
NZP CSI-RS on target cell
  Option 1: Overlaps with PDSCH from interference
  Option 2: Overlaps with NZP CSI-RS from interference
  Option 3: Interference free

## Slide 5: Others
Use LTE test metric as starting point and define based on simulation results.
RAN4 to discuss whether the CQI reporting requirements with inter-cell interference is released independent from Rel-15 or not, after RAN4 agree with the detailed simulation assumption.