## Slide 1: WF on measurement gap issues for eMTC
Nokia Networks, Alcatel Lucent, Intel, Ericsson
R4-77AH-IoT-0140
3GPP TSG-RAN WG4 Meeting NB-IoT
Budapest, Hungary, 20-22 January, 2016
Agenda Item: 3.6

## Slide 2: Background
An MTC UE can only work on a sub-band of 6-PRB.
The MTC UE has to re-tune to the central 6-PRB to perform intra-frequency cell detection and/or measurement.
Re-tuning is achieved using measurement gap.
Discussions related to gap sharing between intra- and inter-frequency RRM, as well as the impact of gap usage to the delay requirement of cell detection and/or measurement have been discussed.

## Slide 3: Agreements
From RAN4 perspective the legacy gap pattern is re-used by Rel-13 MTC UEs for re-tuning to central PRBs dedicated for intra-frequency.
Gap pattern 0 and gap pattern 1 are both valid gap patterns.

## Slide 4: Way Forward
Measurement gap usage/distribution is left to UE implementation as long as the requirements are fulfilled.
Rel-13 solution should not prevent introduction of inter-frequency measurement support in a later release.
  Option 4: techniques for sharing of gaps among intra-frequency and all configured inter-frequency carriers in later release are FFS.