## Slide 1: Way forward on measurement gap timing offset
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, US, January 22nd - January 26th, 2018
R4-1800564
Document for: Approval
Agenda item: 4.6.4

## Slide 2: Background
RAN1#91 agreements:
SMTC window duration:
  Both for inter-/intra- frequency measurements, the candidate values are {1,2,3,4,5} msec
SMTC window timing offset:
  SMTC window timing reference for the timing offset is SFN#0 of the corresponding serving cell.
    Note: For IDLE mode, the serving cell here implies the cell UE is camped on.
  For intra-frequency measurements, the candidate values are {0, 1, …, SMTC periodicity -1} ms
  For inter-frequency measurements, the candidate values are {0, 1, …, SMTC periodicity -1} ms.
15 kHz SCS
30 kHz SCS
120 kHz SCS
5 ms SMTC window
1 ms
Observation: SMTC window timing offset has 1 ms granularity irrespective of FR1/FR2 and SSB SCS

## Slide 3: Problem
UE is not required to perform measurement outside SMTC window
For RRM measurement with measurement gap, UE can perform measurement only in effective measurement duration within measurement gap
For SSB-based measurement with measurement gap, if effective measurement duration within measurement gap and SMTC window duration are not aligned, only overlapped duration is available for measurement and some SSBs in non-overlapped part may be missed
This issue may happen if measurement gap timing offset has 1 ms granularity as in LTE
5 ms SMTC window timing
Example 1: Measurement gap with 6 ms length is starting at the same timing with SMTC window
Example 2: Measurement gap with 6 ms length is starting from 1 ms earlier than SMTC window
6 ms MG timing
Effective measurement duration (excluding RF retuning time)
5 ms SMTC window timing
6 ms MG timing
Effective measurement duration (excluding RF retuning time)
missed
missed
Observation: If MG offset indication has 1 ms granularity as in LTE, the timing of effective measurement duration within MG cannot be aligned with the timing of SMTC window

## Slide 4: Discussion
When SMTC window duration is less than 5 ms, measurement gap with 6/5.5 ms length starting at 1 ms before SMTC window can cover whole SMTC window duration by effective measurement duration
  However, it is inefficient compared with the case of using 4/3.5 ms MGL
  When SMTC duration is 1 or 2 ms, MGL needs to be 3.5 or 4 ms instead of 1.5 or 3 ms
When SMTC window duration is 5 ms, although beginning and ending parts of SMTC window may not contain SSBs, it is not sufficiently long and hence the problem would happen
4 ms SMTC window timing
6 ms MG timing
Effective measurement duration (excluding RF retuning time)
5 ms
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
SSB #0
SSB #1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
SSB #62
SSB #63
120 kHz SCS
About 35.7 us
About 35.7 us
(+ 0.25 ms)
0.25 ms
0.5 ms
0.5 ms
<
>

## Slide 5: Discussion
Possible solution
Support configuration of 0.5 ms or 0.25 ms timing shift for MG timing offset
  MG timing offset signaling granularity can be kept as 1 ms
  -0.5 ms or -0.25 ms timing shift can be enabled/disabled for each UE according to frequency range and UE capability regarding per FR gap
  In case that serving cell slot(s) is/are partially overlapped with MG (e.g., in case of 1 ms slot size), UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH in the slot(s) as well as in serving cell slots that are fully overlapped with MG
Alt: Support finer granularity for MG timing offset (e.g., 0.5 ms or 0.25 ms granularity)
  Signaling size for MG timing offset is increased
  No benefit over above solution
5 ms SMTC window timing
6 ms (5.5 ms) MG timing
Effective measurement duration (excluding RF retuning time)
Serving carrier
Inter-freq carrier
-0.5 ms (-0.25 ms) timing shift
In case of 1ms slot, effective MGL becomes 1 ms longer

## Slide 6: Proposal
Support configuration signaling for MG timing offset with -0.5/-0.25 ms timing shift
  1 bit indication is introduced per MG configuration
    For UE having per FR gap capability, MG timing offset for each MG can be enabled or disabled independently
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on serving cell(s) in slot(s) partially overlapping with MG as well as in slot(s) fully overlapping with MG
  FFS: support of the MG timing offset with -0.5/-0.25 ms timing shift when the MG affects LTE serving cell(s)
Send LS to RAN2