## Slide 1: Way forward on UE behavior during measurement outside measurement gap
NTT DOCOMO
R4-1800566
Document for: Approval
3GPP TSG-RAN WG4 NR-AH#4
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.4.2

## Slide 2: Background
Agreements in RAN4#84bis regarding intra-frequency measurement in FR1 and FR2
It shall be assumed in release 15 that all UE are not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on FR2 serving cells during FR2 intra-frequency measurements, i.e., no capability is needed
For UE not supporting mixed numerology scenarios in FR1 and FR2, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH for intra-frequency measurement without RF-retuning
Agreements in RAN4#85 regarding RX beam switching in FR1
RX beamforming switch in FR1 should not introduce interruption

## Slide 3: Background
Discussion at RAN4#85 (R4-1714288)
Following proposals were discussed
  In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement:
    For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration if useServingCellTimingForSync is enabled
    For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration if useServingCellTimingForSync is not enabled
5 ms SMTC window
Serving cell
Neighbor cells
e.g., 4 ms SMTC window
Not available for data/cont.
Not available for data/cont.
Async case
Sync case

## Slide 4: Background
Discussion at RAN4#85 (R4-1714288)
Following proposals were discussed
  In FR2 intra-frequency SS-RSRP/SINR measurement:
    For UE capable of fast RX beam switching, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration (if useServingCellTimingForSync is enabled)
    For UE not capable of fast RX beam switching, down-select from following two options
      Option 1: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within slots containing SSB symbols to be measured within SMTC window duration (if useServingCellTimingForSync is enabled)
      Option 2: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, X symbol(s) before each consecutive SSB symbols and X symbol(s) after each consecutive SSB symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
        X = [1] symbol for 60 kHz SCS and [2] symbols for 120 kHz SCS

## Slide 5: [Annex]
Cells within a carrier are synchronized (only TDD bands in FR2)
  For UE capable of fast RX beam switching, only SSB symbols to be measured within SMTC window duration are not available for PDCCH/PDSCH/PUCCH/PUSCH
  For UE not capable of fast RX beam switching, SSB symbols to be measured and some additional symbols (before/after SSB symbols) would not be available for PDCCH/PDSCH/PUCCH/PUSCH
e.g., 3 ms SMTC window
Not available for data/cont
Not available for data/cont
e.g., 3 ms SMTC window
Not available for data/cont
Not available for data/cont

## Slide 6: Background
Discussion at RAN4#85 (R4-1714288)
Following proposals were discussed
  In FR2 intra-frequency SS-RSRQ measurement:
    For UE capable of fast RX beam switching, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured and RSSI measurement symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
    For UE not capable of fast RX beam switching, down-select from following two options
      Option 1: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within slots containing SSB symbols to be measured and/or RSSI measurement symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
      Option 2: UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured, RSSI measurement symbols , X symbol(s) before each consecutive SSB/RSSI symbols and X symbol(s) after each consecutive SSB/RSSI symbols within SMTC window duration (if useServingCellTimingForSync is enabled)
        X = [1] symbol for 60 kHz SCS and [2] symbols for 120 kHz SCS

## Slide 7: [Annex]
Agreements on RSSI time resource made at RAN1#91/RAN4#85
When a set of slots for RSSI time-domain measurement resource can be explicitly configured per frequency carrier for a UE in RRC_CONNECTED mode:
  Slots in the RSSI measurement resource are configured by a bitmap with each bit corresponding to each slot of the slots within the SMTC window duration
    Here, the slots are determined based on the SSB numerology
  OFDM symbol level configuration for the configured slots:
    Configurable with a limited set of ending symbols; the set of symbols in a slot is from symbol 0 to the ending symbol
      No more than 4 values for the end symbol
For default RSSI evaluation period, the time duration, TRSSI, is defined as follows:
  TRSSI= Configured SMTC measurement window (if gap is not used)
  TRSSI= Overlapped time span between configured SMTC measurement window and minimum measurement time within measurement gap (if gap is used)

## Slide 8: Discussion
Regarding RX beam switching time, basically all UEs capable of FR2 operation should be able to perform fast RX beam switching
  Otherwise, PDSCH reception after PDCCH reception does not work in the case where PDCCH beam and PDSCH beam are different (it is not minor case)
Since the number of cell searchers at UE would be limited, there is a concern on measurement requirements for the case where SMTC window timings across different intra-freq/inter-freq carriers to be measured are overlapped.
  If SMTC on each serving CC is not aligned as in Case 1, measurement can be performed for each CC in corresponding SMTC timing. However, mixed numerology or analog Rx beam restriction would happen even when measuring other CC (e.g., intra-band CC)
  If SMTC on each serving CC is aligned as in Case 2, measurement would be performed for each CC in different timings. Even in such case, mixed numerology or analog Rx beam restriction would happen e.g., across intra-band CCs
Case 1
Serving #0
Serving #1
Serving #2
Inter-freq
MG
SMTC
SMTC
OK
OK
OK
OK
OK
OK
Case 2
SMTC
OK
OK
SMTC
OK
SMTC
OK
OK
OK
MG

## Slide 9: Discussion
For intra-band CA operation, intra-frequency measurement on only one of serving CCs would be enough in some cases (e.g., co-located CCs)
  Hence, it should be possible to disable intra-frequency measurement on other serving CCs
  It is beneficial not only for case with mixed numerology and/or analog BF restriction but also for general measurement delay for overlapped SMTCs
When there are multiple serving CCs with intra-frequency measurement for intra-band CA, UE would not be able to receive PDSCH/PDCCH during measurement on any one of CCs due to mixed numerology and/or analog BF restriction
CC#1
CC#2
e.g., 3 ms SMTC window with actual SSB index {#1, #3, …, #31} for measurement
e.g., 1 ms SMTC window with actual SSB index {#0, #1, …, #15} for measurement
Not available for data reception on CC#1 due to measurement on CC#2
Not available for data reception on CC#2 due to measurement on CC#1

## Slide 10: Proposal
For non-CA case:
In FR1 intra-frequency SS-RSRP/RSRQ/SINR measurement:
  For UE not supporting mixed numerology scenarios, UE is not expected to receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration if useServingCellTimingForSync is enabled
  For UE not supporting mixed numerology scenarios, UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on all symbols within SMTC window duration if useServingCellTimingForSync is not enabled
In FR2 intra-frequency SS-RSRP/SINR measurement:
  UE is not expected to receive PDCCH/PDSCH on SSB symbols to be measured within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)
In FR2 intra-frequency SS-RSRQ measurement:
  UE is not expected to transmit PUCCH/PUSCH or receive PDCCH/PDSCH on SSB symbols to be measured and RSSI measurement symbols within SMTC window duration (assuming that useServingCellTimingForSync is always enabled for FR2)

## Slide 11: Proposal
For CA case:
NR supports to configure enabling/disabling intra-frequency measurement on NR SCell
  At least if there is other serving cell with intra-frequency measurement for intra-band CA, disabling intra-frequency measurement on NR SCell should be possible
For intra-band CA in FR2,
  in each serving cell, UE is not expected to receive PDCCH/PDSCH on SSB symbols to be measured for any one of intra-frequency measurements within the same band
For intra-band CA in FR1 without UE capability on simultaneous reception of SSB and data with mixed numerologies,
  in each serving cell, UE is not expected to receive PDCCH/PDSCH on SSB symbols to be measured for any one of intra-frequency measurements within the same band if the SSB to be measured has different SCS from that for serving cell data