## Slide 1: Way forward on CSI-RS based measurement in NR
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1800626
San Diego, USA, January22nd – 26th, 2018
Agenda Item: 4.6.5

## Slide 2: Background
When UE has already identified a neighbour cell, UE can directly derive the neighbour cell timing and perform CSI-RS based measurement on the neighbour cell .
When UE is indicated that neighbour cell is synchronous with serving cell, UE can utilize serving cell timing to derive the index of SSB transmitted from the neighbour cell timing.
Otherwise, UE needs to perform SSB detection for the purpose of obtaining sufficient timing information before performing CSI-RS based measurements neighbour cells.

## Slide 3: Consensus
For CSI-RS based measurement, RAN4 is to specify three sets of measurement reporting delay requirements:
  The measurement reporting delay for an identified cell:
    Treporting_delay_w/o_index = TCSI-RS_measurement_period
  The measurement reporting delay for a non-identified cell with synchronous indication:
    Treporting_delay_w/o_index = TPSS/SSS_sync + TCSI-RS_measurement_period
  The measurement reporting delay for a non-identified cell without synchronous indication :
  Treporting_delay_w_index= TPSS/SSS_sync + TSSB_time_index + TCSI-RS_measurement_period
  Where, TPSS/SSS_sync is the time period used in PSS/SSS detection, TSSB_time_index is the time period used to acquire the index of the SSB being measured, and TCSI_RS_measurement_period is the measurement period of CSI-RS based measurement.

## Slide 4: Consensus
The requirements on TPSS/SSS_sync and TSSB_time_index applied for SSB based measurements can be reused for CSI-RS based measurements.
RAN4 need to study the measurement period and measurement accuracy of CSI-RSRP/CSI-RSRQ/CSI-SINR