## Slide 1: Way forward on scope of SA RRM requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #85 San Diego, USA, 22nd – 26th January 2018
Agenda Item: 4.6.1
R4-1800842

## Slide 2: Agreement
The summary of RRM requirement to be defined for SA operation
RRM requirements expected in TS38.133 for enabling SA operation |  |  | 
Types of requirements | Functionalities | Need or not | Agreement
RRC_IDLE state mobility | Cell selection/re-selection, paging interruption | Y | 
RRC_INACTIVE state mobility | Cell selection/re-selection, paging interruption | Y | UE may support different DRX cycles
RRC_CONNECTED state mobility | Handover | Y | Both handover for intra-NR and inter-RAT to E-UTRAN
RRC Connection Mobility Control | RRC re-establishment | Y | 
 | Random access | N | Existing requirements apply for both NSA and SA
UE timing and signalling characteristics | UE transmit timing | N | Existing requirements apply for both NSA and SA
 | UE timer accuracy | N | 
 | Timing advance | N | 
 | Radio link monitoring | N | 
 | Interruption with DC | N/A | 
 | Cell phase synchronization accuracy | N | 
 | PSCell addition/release/change delay | N/A | 
 | Maximum Receive Timing Difference in Dual Connectivity | N/A | 
 | Maximum Transmission Timing Difference in Dual Connectivity | N/A | 
 | NR SCell Activation and Deactivation Delay | N | 
UE Measurements Procedures in RRC_CONNECTED State | Intra/inter-frequency measurement, UE measurement capability | Y | Different scaling factors Nfreq should be used for NSA and SA
RRM requirements expected in TS38.133 for enabling SA operation |  |  | 
RRC_IDLE state mobility | Cell re-selection from E-UTRAN to NR | Y | Support mobility from E-UTRAN to NR
RRC_CONNECTE state mobility | handover from E-UTRAN to NR | Y | Support mobility from E-UTRAN to NR