## Slide 1: WF on maximum channel bandwidth criteria
Skyworks, Huawei, Qorvo, Broadcom, […..]
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, US, 22 - 26 Jan, 2018
R4-1801008

## Slide 2: Background
The mandatory channel bandwidth to be supported by UE was agreed in RAN#78.
At this point no verification was done on the feasibility of the recently introduced channel bandwidths especially for UL where the relative bandwidth to be supported is key in terms of MPR performance (memory effects, bandwidth limitation, output matching Q)
At the time it was agreed that MPR would be constant across channel bandwidths the only cases for large channel bandwidths were associated with TDD bands >2.5GHz thus ensuring low enough relative bandwidth to be supported

## Slide 3: Relative Bandwidth definition
The difficulty of supporting large channel bandwidths depends on a number of factors like:
  Achievable Q in output matching which depends on relative channel bandwidth
  Biasing bandwidth which is constrained in FDD case to achieve low noise emissions in RX channel
  Memory effects which is a combination of the above
Maximum UL Relative Channel bandwidth definition:
  max UL CH BW rel = (2*max CH BW) / (FUL low + FUL high)
For example for band n78:
  n78 max UL CH BW rel = 2*100/(3300+3800) = 2.8%

## Slide 4: Uplink Maximum Relative Channel Bandwidth for Current NR band definitions
In LTE the maximum relative channel bandwidth supported without additional MPR compared to the general MPR requirement is 3% (FDD band 71)
With the currently agreed mandatory channel bandwidths (RP- there is only two cases which exceeds 3%.
  Being TDD bands, the noise in receive is not a concern and 4% relative bandwidth support has been verified on band 41 with measurements
  Still band n50 has a relative max CH BW >5% which cannot be supported without evaluating the need for extra MPR compared to the general MPR.

## Slide 5: Agreement: Maximum Channel Bandwidth Criteria.
In order to introduce new channel bandwidths in the future we propose to introduce a criteria to decide if the general MPR applies or additional MPR should be evaluated:
If max UL CH BW rel ≤3% for FDD bands and ≤4% for TDD bands general MPR requirement applies
If max UL CH BW rel >3% for FDD bands and >4% for TDD bands additional band and channel bandwidth specific MPR should be evaluated

## Slide 6: Agreement: Band n50
To solve the issue that 80MHz channel bandwidth support for band n50 results in max UL CH BW > 5% a few options were discussed including evaluating additional MPR for 80MHz channel bandwidth.
Compromise was reached with band n50 proponent to limit UL channel bandwidth support to 60MHz which results in 4.1% max UL CH BW rel which is acceptable for TDD band and close enough to the 4% criteria.

## Slide 7: References
RP-172832, WF on Channel Bandwidth Support for NR, Qualcomm Incorporated, Sprint, Nokia, Nokia Shanghai Bell, Deutsche Telekom, Orange, Telecom Italia, BT, AT&T, T-Mobile US, Dish Network, Verizon, RAN#78
R4-1800534, Analysis of NR Relative Transmission Bandwidth and its Potential Impact on MPR and MSD, Skyworks, RAN4#AH-1801
R4-1706321, WF on Channel Bandwidth, Qualcomm, RAN4 #83
  The maximum channel bandwidth supported by UE can be different for UL & DL and SCS specific.