## Slide 1: WF on Inter-RAT Requirements in NR SA and NSA Operation
Ericsson, Intel, Nokia
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, USA, January 22-26, 2018
R4-1801049

## Slide 2: Inter-RAT Requirements in NR SA
In NR standalone (SA) operation the UE is configured with at least NR PCell
In this case the inter-RAT requirements shall be defined to support mobility between NR and E-UTRAN in Rel-15:
  The corresponding inter-RAT E-UTRA requirements shall be defined in RRC IDLE, RRC_INACTIVE and RRC CONNECTED states in TS 38.133:
  The corresponding inter-RAT NR requirements shall be defined in RRC IDLE and RRC CONNECTED states in TS 36.133:
See details on slides # 4 and # 5

## Slide 3: Inter-RAT E-UTRA Requirements in SA in TS 38.133
Inter-RAT E-UTRA requirements needed for mobility from NR to E-UTRAN in TS 38.133:
No. | Requirements in RRC IDLE and INACTIVE States (TS 38.133) | Comments
1-1 | Measurements of inter-RAT E-UTRAN FDD/TDD cells | Measurement on RSRP and RSRQ
1-2 | UE measurement capability | No. of E-UTRA FDD/TDD carriers to monitor
1-3 | Maximum interruption in paging reception | Details are FFS
No. | Requirements in RRC CONNECED State (TS 38.133) | Comments
1-4 | NR – E-UTRAN FDD/TDD Handover | Details are FFS
1-5 | RRC Connection Release with Redirection to E-UTRAN FDD/TDD | Details are FFS
1-6 | Applicable Gap Pattern Configurations | As defined in Table 9.1.2-2 in TS 38.133
1-7 | UE measurement capability | - No. of E-UTRA FDD/TDD carriers to monitor - Maximum allowed layers for multiple monitoring
1-8 | NR – E-UTRAN FDD/TDD Measurements | Cell search and RSRP/RSRQ L1 period
1-9 | Event Triggering and Reporting Criteria | Ecat = 10 per RAT (E-UTRA TDD or FDD)
Note: Other inter-RAT E-UTRA requirements are not precluded depending on procedures defined in RAN1/RAN2

## Slide 4: Inter-RAT NR Requirements in SA in TS 36.133
Inter-RAT NR requirements needed for mobility from E-UTRAN to NR in TS 36.133:
No. | Requirements in RRC Idle and Inactive States (TS 36.133) | Comments
2-1 | Measurements of inter-RAT NR cells | Measurement on SS-RSRP and SS-RSRQ
2-2 | UE measurement capability | No. of NR carriers to monitor
2-3 | Maximum interruption in paging reception | Details are FFS
No. | Requirements in RRC Connected State (TS 36.133) | Comments
2-4 | E-UTRAN FDD/TDD – NR Handover | Details are FFS
2-5 | Applicable Gap Pattern Configurations | As defined in Table 8.1.2.1-1 in TS 36.133
2-6 | UE measurement capability | - No. of NR carriers to monitor - Maximum allowed layers for multiple monitoring
2-7 | E-UTRAN – NR Measurements | Cell search and SS-RSRP/SS-RSRQ/SS-SINR L1 period
2-8 | Event Triggering and Reporting Criteria | Ecat = 10 per RAT (NR TDD or FDD)
Note: Other inter-RAT E-UTRA requirements are not precluded depending on procedures defined in RAN1/RAN2

## Slide 5: Inter-RAT Requirements in NSA
In non-standalone (NSA) operation the UE is configured with at least E-UTRA PCell and NR PSCell i.e. EN-DC operation.
In this case the inter-RAT requirements shall be defined RRC CONNECTED states in TS 36.133 in Rel-15 to support mobility between:
  E-UTRA FDD/TDD and GSM,
  E-UTRAN FDD/TDD and UTRAN FDD and
  E-UTRAN FDD/TDD and UTRAN TDD
See details on slides # 6, # 7 and # 8.
Requirements for inter-RAT CDMA2000 and HRPD in EN-DC are FFS

## Slide 6: Inter-RAT GSM Requirements in NSA in TS 36.133
Inter-RAT GSM requirements needed for mobility from E-UTRAN to GSM in TS 36.133:
No. | Requirements in RRC Connected State (TS 36.133) | Comments
3-1 | E-UTRAN FDD/TDD – GSM Handover | Existing requirements in 36.133 apply in EN-DC
3-2 | RRC connection release with redirection to GERAN | Existing requirements in 36.133 apply in EN-DC
3-3 | Applicable Gap Pattern Configurations | Gap id # 0 and # 1 for GSM measurements
3-4 | UE measurement capability | - No. of GSM carriers (GSM layer corresponds to 32 carriers) to monitor - Maximum allowed layers for multiple monitoring
3-5 | E-UTRAN FDD/TDD – GSM measurements | GSM RSSI measurement period, BSIC confirm and re-confirm; scaling of requirements by NFreq,NSA
3-6 | Event Triggering and Reporting Criteria | Ecat = 5 (existing requirements in 36.133 apply in EN-DC)

## Slide 7: Inter-RAT UTRAN FDD Requirements in NSA in TS 36.133
Inter-RAT UTRA FDD requirements needed for mobility from E-UTRAN to UTRAN FDD in TS 36.133:
No. | Requirements in RRC Connected State (TS 36.133) | Comments
4-1 | E-UTRAN FDD/TDD – URAN FDD Handover | Existing requirements in 36.133 apply in EN-DC
4-2 | RRC connection release with redirection to UTRAN FDD | Existing requirements in 36.133 apply in EN-DC
4-3 | Applicable Gap Pattern Configurations | Gap id # 0 and # 1 for UTRAN FDD measurements
4-4 | UE measurement capability | - No. of 3 UTRA FDD carriers to monitor - Maximum allowed layers for multiple monitoring
4-5 | E-UTRAN FDD/TDD – UTRAN FDD measurements for mobility | Cell search and CPICH measurements’ L1 period; scaling of requirements by NFreq,NSA
4-6 | E-UTRAN FDD/TDD – UTRAN FDD measurements for SON | Cell search and CPICH measurements’ L1 period; scaling of requirements by NFreq,NSA
4-7 | E-UTRAN FDD/TDD – UTRAN FDD measurements with autonomous gaps (CGI acquisition delay) | Existing requirements in 36.133 apply in EN-DC
4-8 | Event Triggering and Reporting Criteria | Ecat = 5 (existing requirements in 36.133 apply in EN-DC)

## Slide 8: Inter-RAT UTRAN TDD Requirements in NSA in TS 36.133
Inter-RAT UTRA TDD requirements needed for mobility from E-UTRAN to UTRAN TDD in TS 36.133:
No. | Requirements in RRC Connected State (TS 36.133) | Comments
5-1 | E-UTRAN FDD/TDD – URAN TDD Handover | Existing requirements in 36.133 apply in EN-DC
5-2 | RRC connection release with redirection to UTRAN TDD | Existing requirements in 36.133 apply in EN-DC
5-3 | Applicable Gap Pattern Configurations | Gap id # 0 and # 1 for UTRAN TDD measurements
5-4 | UE measurement capability | - No. of 3 UTRA TDD carriers to monitor - Maximum allowed layers for multiple monitoring
5-5 | E-UTRAN FDD/TDD – UTRAN TDD measurements for mobility | Cell search and P-CCPCH RSCP L1 period; scaling of requirements by NFreq,NSA
5-6 | E-UTRAN FDD/TDD – UTRAN TDD measurements for SON | Cell search and P-CCPCH RSCP L1 period; scaling of requirements by NFreq,NSA
5-7 | Event Triggering and Reporting Criteria | Ecat = 5 (existing requirements in 36.133 apply in EN-DC)