## Slide 1: WF on Clarification of UE Measurement Mode
MediaTek
R4-1801071
Document for: Approval
3GPP TSG-RAN WG4 AH1801
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.4.1

## Slide 2: Background
If UE is capable to per-FR-gap, it is capable to operate in both measurement modes.
  Per-UE-gap mode
  Per-FR-gap mode
In NSA, for UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects, there is an ambiguity on which mode to follow if network configures only one measurement gap pattern ID within #0 to #11.
  Note: an MGRP is still needed to provide a reference for UE to meet the requirement for measurements in FR2, although there is no FR2 serving cell

## Slide 3: Background
In NSA, For UE capable to per-FR gap without FR2 serving cells but with both FR1/LTE and FR2 measurement objects,
  Option 1:
    When network configures only the FR1 gap, UE fallbacks to per-UE-gap mode.
  Option 2:
    When network configures only the FR1 gap, UE meets requirements corresponding to an effective MGRP X ms toward FR2 measurement objects.
      X is FFS, e.g., fix a value in spec or follow the MGRP of FR1 gap pattern

## Slide 4: Way forward
Clarification is needed to both UE and network sides.
Option 2 is adopted due to shorter measurement delay and no additional signaling needed.
The effective MGRP X can be further discussed together with the behavior of UE capable for gap-less measurement.