## Slide 1: WF on Types of Intra-frequency Requirements
MediaTek
R4-1801089
Document for: Approval
3GPP TSG-RAN WG4 AH1801
San Diego, US, January 22nd - January 26th, 2018
Agenda item: 4.6.5.2

## Slide 2: Way Forward
Intra-frequency requirement is categorized into 4 types in following table, based on
  frequency domain relationship between SSB and UE active BWP
  time domain relationship between SMTC occasion and measurement gap (MG)
 | Frequency | Time | 
Type 1 | SSB is in UE’s active BWP | SMTC occasion arefully non-overlapped with MG | 
Type 2 |  | SMTC occasion are partially overlapped with MG | 
Type 3 |  | SMTC occasion are fully overlapped with MG | 
Type 4 | SSB is not in UE’s active BWP | SMTC occasion are fully or partially overlapped with MG | 

## Slide 3: Way forward
Type 1: All SMTC occasions are considered for intra-frequency measurement
Type 2: Only those SMTC occasions not covered by gap are considered for intra-frequency measurement.
  Gap sharing is not needed for FR1 without mix numerology
  FFS if gap sharing is needed for FR2 and for mix numerology
Type 3: All SMTC occasions (covered by gap) are considered for intra-frequency measurement
  Gap sharing is needed, or,
  Any other solution is not precluded
Type 4: Only those SMTC occasions covered by gap are considered for intra-frequency measurement.
  Gap sharing is needed

## Slide 4: Way forward
Companies are encourage to provide the requirements in each types in the next meeting.
  FFS if RLM can be further considered together