## Slide 1: WF on Fixed wireless access use case for FR2
Intel Corporation, Verizon
R4-1801104
3GPP TSG-RAN WG4 AH Meeting #1801
San Diego, USA, 22 – 26 January
Agenda item: 4.3.2.1.2

## Slide 2: Background
Co-existence studies on the 55 dBm CPE have concluded with the following outcome [2]:
  Proposal-1: Regarding the required AICR, the ACIR levels in UL for non-collocated case are around 5dB higher than the collocated case when different LSF is considered for victim and interfering network and if we consider the 5% Average throughput loss, the ACIR levels in UL for both collocated and non-collocated case fall in the same range 10dB-15dB as agreed in TR38.803.
  Proposal-2: Regarding receiver dynamic range, minor impact in receiver dynamic range when 55dBm CPE is considered.
  Proposal-3: Regarding in-band receiver blocking, minor impact in receiver in-band blocking when 55dBm CPE is considered.
In RAN4 AH #1801, FR2 power class definition for fixed wireless access (FWA) devices was discussed according to the following:
  Potential definition of a new UE type
  Impact on the UE requirements in TS38.101-2 by the new UE type

## Slide 3: Agreements (1)
UE type
Define a new UE type termed wireless fixed access (WFA)
Impact on UE requirements
The following requirements may be potentially impacted by the new UE type:
  Power class: peak EIRP
  Power class: spherical coverage
  REFSENS
  Whether ACLR is impacted is FFS
  Whether ACS is impacted is FFS
Other potential impacts are not precluded
The requirements associated with the WFA UE type are targeted for the Rel-15 scope of the NR WI
Peak EIRP and EIS evaluation parameters
Verify alignment on any architecture differences and the parameters needed for peak EIRP and EIS calculation of fixed wireless access devices
  Use the table in slide 4 as starting point
As it is not comprehensive, companies are encouraged to provide additional parameters or comments for the table

## Slide 4: Agreements (2)
Parameter | Unit | Comments
Number of antennas in array |  | 
Average element gain | dBi | 
Effective realized antenna array gain | dB | includes frequency roll-off
Polarization properties |  | 
Type of power amplifier |  | distributed
Number of power amplifiers |  | 
Input power delivered to single element | dBm | 
Beamforming feature |  | 
Diversity properties |  | 
Number of receiver chains |  | 
Signal to noise ratio | dB | 
Noise figure | dB | 
Total implementation losses 1 | dB | granularity needed
Note: 1 Includes form factor integration, beam forming and transmission losses |  | 
WFA Peak EIRP and EIS Evaluation Parameters

## Slide 5: Work Plan
RAN4 AH-1801:
Agree on the framework and work plan to implement requirements for the WFA UE type
RAN4 #86:
Finalize the scope of the impact of the WFA UE type on TS38.101-2
Consolidate feedback and finalize parameters to be used in peak EIRP and EIS analysis
Discuss spherical coverage simulation assumptions suitable for the use case
RAN4 #86-Bis:
Make progress on the power class and REFSENS evaluations
Make progress on spherical coverage evaluations
RAN4 #87:
Finalize the requirements for the WFA UE type

## Slide 6
References
# | Tdoc | Title | Source
[1] | R4-1709987 | Simulation assumptions of Co-existence study for 55dBm CPE in mmWave spectrum | Ericsson, Nokia
[2] | R4-1711861 | Summary of simulation results on Coexistence Studies for 55dBm CPE | Ericsson, Qualcomm, Samsung, Verizon, Nokia
[3] | R4-1800160 | Fixed wireless access use case for FR2 power class | Intel corporation