## Slide 1: WF peak EIRP requirement for mmW
Qualcomm, [ ]
R4-1801106
3GPP TSG-RAN WG4 AH meeting
San Diego, USA, 22 - 26 Jan 2018
Agenda item: 4.3.2.1.3

## Slide 2: Background for peak EIRP
Going in to 3GPP WG4#85 Reno
  Intel/Apple proposal was 20.2 dBm QPSK @ 28 GHz
  Qualcomm proposal was 28.2 dBm pi/2 BPSK @ 28 GHz
  Other companies proposals were in between these numbers
Coming out of the meeting compromises were (R4-1714445)
  Intel/Apple 21.2 dBm QPSK @ 28 GHz
  Qualcomm 25.2 dBm QPSK @ 28 GHz
Current 3GPP requirement TS 38.101-2 v15.0.0
  The handheld UE peak EIRP range is in TS 38.101-2
    For 28 GHz: [21.2-25.2] dBm
    For 39 GHz: [19.4-23.7] dBm

## Slide 3: Summary of proposals in AH-1801
Proposals in this meeting for 28 GHz were :
  21.2 dBm R4-1800336, Intel, Apple
  23 dBm R4-1800891, Sony, Ericsson
  21.5 dBm R4-1800513, LG
  35 dBm, R4-1800944, NXP
  25.2 dBm, Verizon
Proposals in this meeting 39 GHz were:
  19.4 dBm R4-1800336, Intel, Apple, R4-1800513, LG
  21 dBm R4-1800891, Sony, Ericsson
  35 dBm, R4-1800944, NXP
  23.7 dBm, Verizon
Additionally there was a compromise proposed by Qualcomm, Motorola Mobility, TMO, Sony, Verizon, KT and AT&T in R4-1800405
  23.2 dBm @ 28 GHz
  21.5 dBm @ 39 GHz

## Slide 4: Summary of proposals in AH-1801
28 GHz [dBm]
  24.85 Average
  23.23 Average excluding lowest and highest value
  23.79 Average weighted by companies
39 GHz [dBm]
  24.12 Average
  22.07 Average excluding lowest and highest value
  22.15 Average weighted by companies

## Slide 5: Discussion on cover loss
Cover loss data has been presented in
  R4-1800889, Impact of UE back cover material on peak EIRP at mmWave, Sony
  R4-1800369, On UE Packaging Loss, Simulation Results, Qualcomm
  R4-1712319, UE power class for FR2, Intel
It was concluded that companies agree with the results of the cover losses if parameters are aligned
There was no agreement what level of cover loss should be allowed to be used in analysis for deriving core requirements

## Slide 6: Offline discussion for peak EIRP
Intel, Apple proposed 21.2 dBm @ 28 GHz and 19.4 dBm @ 39 GHz
Verizon proposed 25.2 dBm @ 28 GHz and 23.7 dBm @ 39 GHz
Number of companies were positive on the compromised proposal in R4-1800405 but no agreement could be reached

## Slide 7: Way Forward
Companies are encouraged to provide further information in upcoming meetings that may assist in decision for peak EIRP requirement
Discussion in upcoming meetings should involve aspects of how much compromise on mmWave performance should be made to benefit design of the phone