## Slide 1: Power Sharing for FR1 EN-DC
InterDigital

## Slide 2: Background
RAN Plenary agreed in December the WF in RP-172833. This WF confirms two types of UEs supporting NSA is FR1.
  Type 1 - capable of dynamic power sharing P_LTE+P_NR>Pcmax
  Type 2 – not capable of power sharing – works always under Pcmax level through configuration P_LTE+P_NR<=Pcmax or in a TDM mode (single uplink)

## Slide 3: RAN 1 – Sub-clause 7.6 from 38.213

## Slide 4: Current concrete proposals for 38.101-3 –AH1801
Qualcomm
  R4-1800398
LGE & InterDigital
  R4-1800519
  R4-1800264 TP for 38.817-01

## Slide 5: Other issues to discuss for EN-DC power sharing
Nokia:
R4-1800068 UE Dynamic power sharing for LTE-NR Dual Connectivity
Huawei:
R4-1800422 on NR EN-DC dynamic power sharing
KDDI:
R4-1800216 Proposals on UE dynamic EN-DC power sharing

## Slide 6: Issues to be resolved for the Pcmax requirement
With RAN1 specification sub-clause 7.6 listed in slide 3, do we have a clear understanding on how to define Pcmax?
Are the proposals from LG/InterDigital in line with 38.213 at least for the case when the UL grants are known for both LTE and NR on time?
Is Qualcomm proposal in line with 38.213?
Can we combine these 2 proposals to cover all the cases?

## Slide 7: Issues to be resolved for P_LTE, P_NR signaling
1. Agree that dedicated signaling of P_LTE and P_NR is needed in RAN4 opinion so that type 1 operation is possible when also type 2 UE’s exists in NW
2. Discussion on defining signaling in LTE and NR RRC that allows setting P_LTE and P_NR per RAT
3. Discuss if LS to RAN2 is needed from this meeting incase item 1 and/or item 2 is agreed
4. Agree that it is network decision when to switch between simultaneous LTE and NR transmissions and TDM based single UL transmission modes (in case P_LTE + P_NR > P_powerclass is configured for type 2 UE
5. Discussion on type 1 UE behavior in case P_LTE + P_NR > P_powerclass i.e. droping or scaling NR transmissions

## Slide 8: Offline Discussion points/outcome
The TPs from Qualcomm, Interdigital/LGE can be merged since both proposals have technical merits.
A second issue discussed was the P_LTE and P_NR signaling:
  Presently, according to 38.213, sub-clause 7.6 gamma_MCG, gama_SCG fractions are used against Pcmax per UE.
  Some companies suggested that they would prefer to have P_LTE and P_NR as absolute levels
    A consequence of P-LTE and P_NR absolute levels signaling agreement would be the insertion of these parameters in the Pcmax equations for LTE in 36.101 and 38.101-1.

## Slide 9: Way Forward for Pcmax
For next meeting:
  The TPs from Qualcomm, Interdigital/LGE can be merged since both proposals have technical merits (to be submitted for next meeting in February).

## Slide 10: Way Forward for P_LTE, P_NR signaling NW/UE behavior