## Slide 1: WF on NR TDD UL/DL configurations and HPUE behavior
Vivo, Qualcomm, Softbank, Sprint
3GPP TSG-RAN WG4 AH-1801 Meeting R4-1801125
San Diego, CA, USA, January 22nd – 26th, 2018

## Slide 2: Background (1)
In order to making sure UE satisfying SAR requirements, HPUE behaviour need to be restricted in RAN4
For LTE, behaviour restriction is by excluding UL/DL configurations 0 and 6 in 36.101 to make sure less than 50% slots are configured for UL
  TDD UL/DL configurations are static broadcasted parameter
For NR, UE supports flexible slots according to semi-static signaling and dynamic signaling. The granularity which can be configured UL/DL or flexible is now symbol rather than slots in LTE
Current RAN4 spec [1] did not consider the NR physical layer changes and need to be refined on this behavior
RAN1 needs feedback on whether new functionality is needed by RAN4 or not [2]

## Slide 3: Background (2)
A discussion paper [3] start discussing this issue. However, no proposals could be agreed at current stage.
A number of concerns were raised regarding possible behaviour restriction.
  If a 50% rule was used, it may imply the UE should do calculation and dynamic / semi-dynamic change on the power class it used. This may introduce complexity and feasibility problem.
  The “flexible” symbol may be dynamically scheduled as UL/DL/blank. This uncertainty raise concerns for the behaviour restriction either more strict than needed or risky of failing regulatory requirements

## Slide 4: Way Forward
Companies are encouraged to study the following options for HPUE :
  Option 1：Do not restrict the Slot Formats;
    Based on counting less than 50% UL duty cycle with a granularity of symbols;
    How to treat “flexible” symbol and appropriate evaluation period need to be solved.
  Option 2：Select an allowed subset of Slot Formats;
    Using fixed slot formats which is similar to LTE’s scheme
    Try to circumvent the dilemma of how to treat “flexible” symbol and finding appropriate evaluation period.
    New formats may be recommended by RAN4 if deemed necessary
Other options are not precluded.
Feedback to RAN1 after RAN4 reach conclusion.

## Slide 5: References
[1] TS 38.101-1, V15.0.0
[2] R1-1721538, “[Draft] LS on NR TDD UL/DL configurations and support of HPUE,” SoftBank & Sprint, 3GPP RAN1 #91, November 26th – December 1st 2017
[3] R4-1800414, “Discussion on NR TDD UL/DL configurations and HPUE behaviour”, vivo, 3GPP TSG-RAN WG4 AH-1801 Meeting, January 22nd – 26th, 2018