## Slide 1: WF on PA calibration gap parameters
Qualcomm, Intel Corporation, [ ]
R4-1801135
3GPP TSG-RAN WG4 AH meeting
San Diego, USA, 22 - 26 Jan 2018
Agenda item: 4.3.2.9.1.1.3

## Slide 2: Background
PA Calibration gap has been shown to improve FR2 UE performance
  [1] R4-1800125, PA calibration gap for FR2, Intel
  [2] R4-1800387, PA Calibration gap parameters for FR2, Qualcomm
Parameters have been proposed in contributions above for
  Gap duration
  Gap periodicity
  Gap scheduling criteria in other conditions such as power or RB allocation chance
  UE capability
UE behavior was discussed when
  UE identifies it needs gap but network does not schedule it
  UE has only one TX and needs a total TX gap
Impact on system performance is yet to be determined

## Slide 3: Way Forward on calibration gap feature
The need for UE calibration gap is a UE capability
  The capability definition is per UE as a baseline assumption
  Companies are encouraged to provide additional analysis whether a per-band definition is needed or if the baseline assumption can be confirmed next meeting
With capability, UE informs network if it needs gap for one TX at a time as described in [1] or for all TX ports simultaneously i.e. total no UL at all gap
The virtue of the calibration gap feature is to be assessed w r t
  other methods not requiring scheduled gaps e.g. use of the ordinary transmitted signal and run the calibration during normal UL transmission
  impact of scheduled gaps on the system performance (e.g. scheduling of other users not calibrating their PA)
  impact to UE behaviors/requirements when the gaps are not scheduled by gNB.
Interested companies are encouraged to provide analysis of the impact of scheduled gaps on system performance according to
  Scheduler complexity
  UE implementation complexity and power consumption
  Impact on gap parameter values
  Definition of gap configuration fall-backs, if needed
LS to inform RAN2 and RAN1 about new capability shouldwill be sent with the information above pending discussions at upcoming meetings

## Slide 4: Way Forward on parameters for calibration gap
Gap duration is one slot i.e. no UL for this UE is scheduled for contiguous duration of 14 symbols
Gap periodicity
  Periodicity can be fixed (allocated by the network) or depend on number of parameters (when triggered by the UE)
  For gaps with fixed periodicity, the gap period is at most 8,000 slots (1000 ms with 60 kHz SCS / 500 ms with 120 kHz SCS) or periodicity is defined as UE capability
For gaps triggered by the UE, details are FFS other events, UE power or UE TX BW change, network assigns gaps based on information from UE reports or UL grant information
Gap is applied only when UE is operating at relatively high power level
  Details FFS

## Slide 5: Way Forward on requirement impact
Two output power requirements will be defined:
  1) UE with calibration gap and proper scheduling of gap from network
  2) UE with calibration gap but no gap is scheduled
The impact of the PA calibration gap feature on UE RF requirements in TS38.101-2 is as follows:
  A single MPR table is defined for all UEs whether they support the PA calibration gap or not
    Assumption for MPR work is that UE applies calibration
  Test case parameters associated with output power requirements are updated to include PA calibration gap configuration for the applicable UEs, such that
    Gaps with fixed periodicity are allocated in the test case configuration
  How to define a requirement for gaps triggered by other events the UE is FFS