## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1801293 San Diego, US, 22 - 26 Jan, 2018
Agenda item: 4.2.1
Document for: Approval
WF on mixed numerology for CA
Huawei, HiSilicon

## Slide 2: Background
RAN #78 agreement:
  For NR-NR CA, finalization of the work to enable up to 2 different numerologies within the same PUCCH group (PUCCH sent on the CC with smaller SCS) in RAN1 in Q1, and in RAN4 (Core) for Q2, for the December drop.
Reference:
R4-1800421 on mixed numerology for CA, Huawei, HiSilicon
R4-1800516 Some clarifications for wideband operation of NR UE, LG

## Slide 3: Agreement
RAN4 agreement copied from chairman notes:
Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15.

## Slide 4: WF(1)
Intra-band CA:
  Option 1: Introduce mixed numerology as UE capability in Rel15
  Option 2: it is not supported on mixed numerology in Rel15 for intra-band CA
  RAN4 will make a decision in the next meeting
Wideband operation with contiguous UE CCs: reuse intra-band contiguous CA case

## Slide 5: WF(2) for Inter-band CA
Band | Band | Same numerology | 2 numerologies
FR1 | FR1 | Mandated for CA | FFS
FR1 | FR2 | No | Mandated for CA
FR2 | FR2 | Mandated for CA | With UE capability

## Slide 6: WF(3)
Signalling of SCS for CA:
  Option 1: Signaling of SCS per CC in BPC/BPC entry(baseband processing capabilities)
  Option 2: Signaling of SCS per BC
  Option 3: Signaling of SCS per UE: report UE capability on mixed numerology for CA per UE regardless of BC
  Option 4: Signaling of SCS per Band
Companies are encouraged to provide further analysis for the down selection for signaling of SCS based on the above 4 options.