## Slide 1: Way forward on the performance part side conditions
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #AH1807 Montreal, Canada, 2nd – 6th July, 2018
Agenda item: 5.3.2
R4-1809036

## Slide 2: Background
The difference between NR and LTE in defining the side conditions for measurement accuracy requirements is that in NR the REFSENS is not only band agnostic but also depends on the subcarrier spacing used.
The reason for this is that when configured with different SCS, the bandwidth of the resource blocks are slightly different resulting in the slightly difference in REFSENS.

## Slide 3: Way forward
Define band groups with regard to the REFSENS of the NR operating bands and reuse the LTE band group table as the baseline.
When defining performance part requirements for NR, use one of the below methods to define minimum Io levels with the SCS scaling
  Enumeration of SCS values
  Equations with variable of SCS value
When defining side conditions in test cases for NR, use one of the below methods to define minimum Io levels with the SCS scaling
  Enumeration of SCS values
  Equations with variable of SCS value

## Slide 4: Annex: examples of methods to define side conditions with different SCS
Enumeration of SCS values
  E.g.,
Accuracy |  | Conditions |  |  |  |  | 
Normal condition | Extreme condition | Ês/Iot Note 2 | Io Note 1 range |  |  |  | 
 |  |  | NR operating band groups | Minimum Io |  |  | Maximum Io
dB | dB | dB |  | dBm/SSB sub carrier spacing |  |  | dBm/BWChannel
 |  |  |  | 15k | 30k | 60k | 
[2] | [3] | [-3] dB | NRFDD_A, NRTDD_A | TBD | TBD | TBD | -50
 |  |  | NRFDD_B | TBD | TBD | TBD | -50
 |  |  | NRTDD_C | TBD | TBD | TBD | -50
 |  |  | NRTDD_D | TBD | TBD | TBD | -50
 |  |  | NRFDD_E1, NRFDD_E2, NRTDD_E2 | TBD | TBD | TBD | -50
 |  |  | NRFDD_G1, NRFDD_G2 | TBD | TBD | TBD | -50
 |  |  | NRFDD_H | TBD | TBD | TBD | -50
 |  |  | NRFDD_A, NRTDD_A | TBD | TBD | TBD | -50
[3] | [3] | [-6] dB | Note 3 | Note 3 |  |  | Note 3
NOTE 1: Io is assumed to have constant EPRE across the bandwidth. NOTE 2: The parameter Ês/Iot is the minimum Ês/Iot of the pair of cells to which the requirement applies. NOTE 3: The same bands and the same Io conditions for each band apply for this requirement as for the corresponding highest accuracy requirement. |  |  |  |  |  |  | 

## Slide 5: Annex: examples of methods to define side conditions with different SCS
Equations with variable of SCS value
  E.g., in the table F(x, y) denotes the minimum Io conditions for band group x and SCS value y.
Accuracy |  | Conditions |  |  | 
Normal condition | Extreme condition | Ês/Iot Note 2 | Io Note 1 range |  | 
 |  |  | NR operating band groups | Minimum Io | Maximum Io
dB | dB | dB |  | dBm/SSB sub carrier spacing | dBm/BWChannel
[2] | [3] | [-3] dB | NRFDD_A, NRTDD_A | F(x, y) | -50
 |  |  | NRFDD_B |  | -50
 |  |  | NRTDD_C |  | -50
 |  |  | NRTDD_D |  | -50
 |  |  | NRFDD_E1, NRFDD_E2, NRTDD_E2 |  | -50
 |  |  | NRFDD_G1, NRFDD_G2 |  | -50
 |  |  | NRFDD_H |  | -50
 |  |  | NRFDD_A, NRTDD_A |  | -50
[3] | [3] | [-6] dB | Note 3 | Note 3 | Note 3
NOTE 1: Io is assumed to have constant EPRE across the bandwidth. NOTE 2: The parameter Ês/Iot is the minimum Ês/Iot of the pair of cells to which the requirement applies. NOTE 3: The same bands and the same Io conditions for each band apply for this requirement as for the corresponding highest accuracy requirement. |  |  |  |  |