## Slide 1: Way forward on NR UE CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting AH 1807
Montreal, Canada, 2 – 6 July 2018 Agenda Item: 5.4.1.3
R4-189358

## Slide 2: Test Scope
Previous agreements
  Overall Test Configuration & Scope
    First priority focused on:
      NZP CSI-RS for channel measurement CSI-IM for interference measurement
      CSI report types: periodic CSI report and aperiodic CSI report
      CSI-RS resources types: periodic and aperiodic
    Rel-15 only focused on Type 1 single panel codebook
On-line agreements
  Rel-15 focused on 1 NZP CSI-RS resource and 1 CSI-IM resource configuration for CSI report. CSI-IM used for interference measurement.
  Rel-15 focused on single BWP/CC with 1 CSI reporting configured
Proposal
  FFS whether to introduce CSI test cases for semi-persistent CSI reporting type
  FFS whether to introduce CSI test cases for semi-persistent NZP CSI-RS resource
  FFS whether to introduce CSI test cases for CRI/CSI reporting
  FFS whether to introduce CSI test cases for CRI/L1-RSRP reporting

## Slide 3: Generic test set-up
On-line agreement:
  CHBW &SCS
    FR1 FDD: 15kHz & 10MHz
    FR1 TDD: 30kHz & 40MHz
    FR2: 120kHz &100MHz
  CQI table
    For FR1 CQI table 2
    For FR2 CQI table 1
Proposals
  TDD DL-UL configuration:
    FOLLOWING agreements and principles FROM PDSCH demod configurations
    FFS on how to down selection from PDSCH dedmod configurations if multiple configurations introduced in demod test cases
  Receiver assumption:
    1 layer: MMSE-IRC
    2,3,4 layers: [MMSE-IRC]

## Slide 4: CQI Test cases
On-line agreements:
  MIMO Tx Rx
    For FR1: 2*2, 2*4
    For FR2: 2*2
  Introduce test cases for wideband, FFS for sub-band
Proposals
  In Rel-15 introduce below CQI test cases
    Wideband static CQI test cases
    Wideband fading CQI test cases
    FFS for sub-band CQI test cases
  Test metric
    Static CQI: reuse LTE as starting point
      The wideband CQI1 shall be within the set {median CQI1 -1, median CQI1, median CQI1 +1} for more than [90% ] of the time
      For both codewords #0 and #1, the PDSCH BLER using the transport format indicated by the respective median CQI0 – 1 and median CQI1 – 1 shall be less than or equal to [0.1]. Furthermore, for both codewords #0 and #1, the PDSCH BLER using the transport format indicated by the respective median CQI0 + 1 and median CQI1 + 1 shall be greater than or equal to [0.1].
    Fading CQI: reuse LTE as starting point
      a) a CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least a % of the time;
      b) the ratio of the throughput obtained when transmitting the transport format indicated by each reported wideband CQI index and that obtained when transmitting a fixed transport format configured according to the wideband CQI median shall be ≥ g ;
      c) when transmitting the transport format indicated by each reported wideband CQI index, the average BLER for the indicated transport formats shall be greater or equal to [0.02].
    Note: Not exclude any other proposals based on further study
  Companies are encouraged to bring results for median CQI +/-1 and BLER and Fading CQI: Relative throughput ratio between following CQI and median CQI

## Slide 5: PMI test cases
On-line agreements
  FR1 MIMO TxRx: 4*2,4*4, 8*2, 8*4
    8 Tx only wideband PMI reporting
    FFS for upper to 32 ports
  FR2 MIMO TxRx : 2*2
  Wideband and FFS for sub-band
Proposals
  In Rel-15 at least introduce below test cases
    4Tx Sub-band PMI test cases for FR1 (phase two)
    4Tx wideband PMI test cases for FR1
    4Tx PMI test cases for FR1
      FFS for wideband and sub-band
    8Tx Wideband PMI test case for FR1
    2Tx wideband PMI test case for FR2
  FFS for 16,32 Tx ports test cases in FR1
  Test metric: reusing LTE as starting point( Relative Throughput ratio between following PMI and random PMI under FRC)
  Codebook construction parameters: (N1,N2), (O1,O2)
    4 Tx ports: (N1,N2) = (2,1), (O1, O2) = (4,-)
    8 Tx ports: (N1,N2) = (2,2)/(4,1), (O1, O2) = (4,4)/(4,1)
      FFS for both or only one
    Sub-mode 1
  FRC (for initial simulation purpose, further down selection between below options and other options not excluded)
    Option 1: MCS 4 rank1
    Option 2: MCS 13 rank2
  For simulation purpose, companies are encouraged to provide following PMI and random PMI results

## Slide 6: RI test cases
On-line agreements
  Number of Rank layers
    FR1 : 1,2,3,4
    FR2: 1,2
Proposals
  In Rel-15 at least introduce below test cases
    FR1:
      2*2 for upper to Rank 2 test
      4*4 for upper to Rank4 test
    FR2:
      2*2 for upper to Rank2 test
  Test metric: using LTE as starting point, FFS for test point(s)
    a) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 1 shall be ≥ g1;
    b) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 2 shall be ≥ g2;
  For simulation purpose, companies are encouraged to provide following Rank, fixed rank1 and fixed rank2 results, FFS for Rank3, Rank4

## Slide 7: Summary of Test case list(Proposals)
Static CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband PMI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 2: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 3: FR2 100MHz& 120kHz, 2*2
4Tx PMI test cases (FFS for wideband or sub-band)
  Test 1: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 2: FR1 TDD 40MHz&30kHz, 4*2, 4*4
Sub-band CQI test cases (2nd priority)
  Test 1: FR1 FDD 10MHz&15kHz, 2*2,2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2,2*4
RI test
  Test 1: FR1 FDD 10MHz&15kHz, 2*2,4*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 4*4
  Test 3: FR2 100MHz&120kHz, 2*2

## Slide 8: Initial Simulation assumption for Static CQI (information)
Parameter | Unit | Static CQI test (FR1 FDD) | Static CQI test (FR1 TDD) | Static CQI test (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | FFS | FFS
Propagation channel |  | AWGN | AWGN | AWGN
Correlation and antenna configuration |  | 2Rx 2*2 with [ ] 4Rx: 2*4 with [ ] | 2Rx 2*2 with [ ] 4Rx: 2*4 with [ ] | 2Rx 2*2 with FFS
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | [5/0] | [5/0] | [5/0]
NZP CSI-RS ports |  | 2 port {3000,3001} | 2 port {3000,3001} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [FD-CDM2/density 1] | [FD-CDM2/density 1] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | 010000 (fixed rank2) | 010000 (fixed rank2) | 010000 (fixed rank2)
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 9: Initial Simulation assumption for wideband fading CQI (information)
Parameter | Unit | Fading CQI test (FR1 FDD) | Fading CQI test (FR1 TDD) | Fading CQI test (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | FFS | FFS
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | FFS
Correlation and antenna configuration |  | 2Rx 2*2 4Rx: 2*4 [ULA High] | 2Rx 2*2 4Rx: 2*4 [ULA High] | 2Rx 2*2 FFS
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5/0 | 5/0 | 5/0
NZP CSI-RS ports |  | 2 port {3000,3001} | 2 port {3000,3001} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [FD-CDM2/density 1] | [FD-CDM2/density 1] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | 000001 | 000001 | 000001
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 10: Initial Simulation assumption for Wideband PMI (information)
Parameter | Unit | Test 1 (FR1 FDD) | Test 2 (FR1 TDD) | Test 3 (FR2)
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | FFS | FFS
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | FFS
Correlation and antenna configuration |  | 8*2 8*4 [XP spatially High] | 8*2 8*4 [XP spatially High] | 2*2 FFS
CSI-RS resource setting (aperiodic) |  |  |  | 
resourceConfigType |  | aperiodic | aperiodic | aperiodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5/0 | 5/0 | 5/0
NZP CSI-RS ports |  | 8 port {3000…3007} | 8 port {3000…30007} | 2 port {3000,3001}
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | [CDM4,density 1 (row 9)] | [CDM4,density 1 (row 9)] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (aperiodic) |  |  |  | 
reportConfigType |  | aperiodic | aperiodic | aperiodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
(N1,N2) |  | (2,2) | (2,2) | N.A
(O1,O2) |  | (4,4) | (4,4) | N.A
CodebookMode |  | 1 | 1 | N.A
Codebook Restriction |  | FFS | FFS | FFS
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Rank |  | 1/2 | 1/2 | 1/2
FRC |  | MCS4/MCS13 | MCS4/MCS13 | MCS4/MCS13
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM

## Slide 11: Initial Simulation assumption for RI (information)
Parameter | Unit | Test 1 (FR1 FDD) | Test 2 (FR1 FDD) | Test 3 FR2
System parameter |  |  |  | 
Bandwidth/SCS | MHz/kHz | 10MHz /15kHz | 40MHz/30kHz | 100MHz/120kHz
Transmission Scheme |  | 1 | 1 | 1
Duplex Mode |  | FDD | TDD | TDD
DLUL configuration |  | N.A | FFS | FFS
Propagation channel |  | TDL_A 30ns, 5Hz | TDL_A 30ns, 10Hz | FFS
Correlation and antenna configuration |  | 2Rx 2*2 4Rx: 4*4 [ULA Low ULA High] | 2Rx 2*2 4Rx: 4*4 [ULA Low ULA High] | 2Rx 2*2 FFS
CSI-RS resource setting (periodic) |  |  |  | 
resourceConfigType |  | Periodic | Periodic | Periodic
CSI-RS/CSI-IM periodicity and slot offset |  | 5/0 | 5/0 | 5/0
NZP CSI-RS ports |  | 2/4 | 2/4 | 2
NZP CSI-RS configuration CDM type/CSIRS resource mapping/CSI-RS-Density |  | 2 ports: [FD-CDM2/density 1] 4 ports: [FD-CDM2 density 1 (row 4)] | 2 ports: [FD-CDM2/density 1] 4 ports: [FD-CDM2 density 1 (row 4)] | [FD-CDM2/density 1]
CSI-IM configuration |  | FFS | FFS | FFS
CSI report setting (periodic) |  |  |  | 
reportConfigType |  | periodic | periodic | periodic
Reporting periodicity and slot offset |  | FFS | FFS | FFS
Codebook Restriction |  | FFS | FFS | FFS
Reporting granularity |  | Wide-band | Wide-band | Wide-band
Physical channel for reporting |  | PUSCH | PUSCH | PUSCH
PUCCH reporting format |  | FFS | FFS | FFS
CQI table |  | Table 2 with 256QAM | Table 2 with 256QAM | Table 1 without 256QAM