## Slide 1: 3GPP TSG-RAN WG4 Meeting #87AH Montreal, Canada, 2 July– 6 July, 2018
Qualcomm, Ericsson, Huawei
Way forward on reference channels for sTTI demodulation and CSI requirements
R4-1809375

## Slide 2: Slot-based PDSCH demodulation requirements
In slot-based PDSCH test cases, for a TB first transmitted at slot n (=0,1), any retransmission can only happen on the slots satisfying following table
When the NAK is received at slot m, retransmission can happen no earlier than slot m+4
Slot for the initial transmission | Slots used for the retransmission
Slot 0 | Slot 0
Slot 1 | Slot 1

## Slide 3: Subslot-based PDSCH demodulation requirements
In subslot-based PDSCH test cases, for a TB first transmitted at subslot n (=1,2,3,4,5), any retransmission can only happen on the subslots satisfying following table
When the NAK is received at sub-slot m, retransmission can happen no earlier than sub-slot m+4 or m+6, depending on UE capability
Subslot for the initial transmission | Subslots used for the retransmission
Subslot 1 | Subslot 1, Subslot 5
Subslot 2 | Subslot 2, Subslot 4
Subslot 3 | Subslot 3
Subslot 4 | Subslot 2, Subslot 4
Subslot 5 | Subslot 1, Subslot 5

## Slide 4: Slot/Subslot-PDSCH demodulation requirements
No PDSCH allocation on subframe 0 and subframe 5 for all sPDSCH test cases
Target coding rate 0.45 for subslot-based CRS-based PDSCH demodulation
Consider 2 NZP CSI-RS ports for DMRS-based slot/subslot-PDSCH test cases
Companies are encouraged to provide the simulation results of sPDSCH based on the agreement
Simulation assumption: R4-1805493

## Slide 5: CQI reporting requirements
Consider following CRS-based sPDCCH config with aggregation level 4
for CRS-based CQI
reporting test
Consider following CRS-based sPDCCH config with aggregation level 8
for DMRS-based CQI
reporting test
 | SPDCCH parameters
Reference symbol | CRS
Transmission type | Localized
Number of OFDM symbols | 1
Number of PRBs | 16
Allocated PRBs | {0, 1, … 15}
Rate matching mode | Mode 1
SPDCCH L1 Reuse Indication | Not configured
Total number of SCCEs | 4 (16 SREGs)
 | SPDCCH parameters
Reference symbol | CRS
Transmission type | Localized
Number of OFDM symbols | 2
Number of PRBs | 16
Allocated PRBs | {0, 1, … 15}
Rate matching mode | Mode 1
SPDCCH L1 Reuse Indication | Not configured
Total number of SCCEs | 8 (32 SREGs)

## Slide 6: CQI reporting requirements
No PDSCH allocation on subframe 0 and subframe 5 for all CQI reporting test cases
No DMRS sharing in TM9 CQI reporting test
Companies are encouraged to provide:
  CQI2MCS mapping table
  Simulation results of CQI reporting
  Proposal of test points
Simulation assumption: R4-1805493

## Slide 7: FRC table for slot-based CRS-based PDSCH (For information)
Sub-frame | Slot index | Information bit payload per slot (for dual layer) | Binary channel bits per slot (for dual layer)
1,2,3,4,6,7,8,9 | 0 | 11448 | 22400
 | 1 | 14112 | 28288
The following FRC table is based on 16QAM modulation and target coding rate 1/2

## Slide 8: FRC table for subslot-based CRS-based PDSCH (For information)
The following FRC table is based on 16QAM modulation and target coding rate 0.45
Sub-frame | Subslot index | Information bit payload per subslot (for dual layer) | Binary channel bits per subslot (for dual layer)
1,2,3,4,6,7,8,9 | 1 | 5160 | 12032
 | 2 | 3880 | 8832
 | 3 | 2664 | 5888
 | 4 | 3880 | 8832
 | 5 | 5160 | 12288

## Slide 9: FRC table for slot-based DMRS-based PDSCH (For information)
Sub-frame | Slot index | Information bit payload per slot (for dual layer) | Binary channel bits per slot (for dual layer)
1,3,4,6,8,9 | 0 | 3624 | 10000
 | 1 | 4392 | 13360
2,7 (2 NZP-CSI-RS ports) | 0 | 2856 | 9600
 | 1 | 4392 | 13360
The following FRC table is based on QPSK modulation and target coding rate 1/3

## Slide 10: FRC table for subslot-based DMRS-based PDSCH (For information)
The following FRC table is based on QPSK modulation and target coding rate 1/3
Sub-frame | Subslot index | Information bit payload per subslot (for dual layer) | Binary channel bits per subslot (for dual layer)
1,3,4,6,8,9 | 1 | 1736 | 4960
 | 2 | 1192 | 4032
 | 3 | 776 | 2688
 | 4 | 1192 | 4032
 | 5 | 1736 | 5088
2,7 ( 2 NZP-CSI-RS ports) | 1 | 1736 | 4960
 | 2 | 1192 | 3696
 | 3 | 776 | 2688
 | 4 | 1192 | 4032
 | 5 | 1736 | 5088

## Slide 11: CQI reporting test for slot-based CRS-based (For information)
Sub-frame | Slot index | Available REs
1,2,3,4,6,7,8,9 | 0 | 2800
 | 1 | 3672

## Slide 12: CQI reporting test for subslot-based CRS-based (For information)
Sub-frame | Subslot index | Available REs
1,2,3,4,6,7,8,9 | 1 | 1408
 | 2 | 1008
 | 3 | 872
 | 4 | 1008
 | 5 | 1472

## Slide 13: CQI reporting test for slot-based DMRS-based (For information)
Sub-frame | Slot index | Available REs
2,3,4,7,8,9 | 0 | 2600
 | 1 | 3348
1,6 ( 2 NZP-CSI-RS ports) | 0 | 2500
 | 1 | 3348

## Slide 14: CQI reporting test for subslot-based DRMS-based (For information)
Sub-frame | Subslot index | Available REs
2,3,4,7,8,9 | 1 | 1180
 | 2 | 680
 | 3 | 612
 | 4 | 680
 | 5 | 1212
1,6 ( 2 NZP-CSI-RS ports) | 1 | 1180
 | 2 | 612
 | 3 | 612
 | 4 | 680
 | 5 | 1212