## Slide 1: Way forward on RRM test configurations
Ericsson
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809400

## Slide 2: Agreements on RMC for RRM test
SS/BPCH block scheduling
  Periodicity: 20ms
  Configure 1 SS/PBCH block per cell for FR1, and [up to 2] SS/PBCH block(s) for each different AoA for FR2
PDCCH/PDSCH is not transmitted inside the SMTC window in time domain due to the scheduling restriction between SS/PBCH and PDCCH/PDSCH
RMC configurations (SCS and Channel bandwidth):
  SCS=15kHz with 10MHz for FDD and TDD (FR1)
  SCS=30kHz with 40MHz for TDD (FR1)
  SCS=120kHz with 100MHz for TDD (FR2)

## Slide 3: Remaining issues on RMC for RRM test
TDD configurations
RMSI CORESET scheduling
PDSCH resource allocation and MCS
  Example: Allocate 24PRB for PDCCH/PDSCH and set 1/3 QPSK for PDSCH MCS (same as LTE RMC)
  Location of PDCCH/PDSCH in frequency domain in the cell in the slots where SS/PBCH block is scheduled and where SS/PBCH block is not scheduled.
DL power allocation
  Note UE RF/Demod session agreed with the DL power allocation (R4-1809332).