## Slide 1: Way forward on gap sharing scheme
NTT DOCOMO
3GPP TSG-RAN WG4 NR-AH#1807
Montreal, Canada, July 2nd - 6th, 2018
R4-1809402
Document for: Approval

## Slide 2: Background
For the sharing of per FR gap for FR2 between NR intra-freq and inter-freq measurements,
  Following definition of gap sharing schemes as in current specification should be fine
Gap sharing scheme | Definition
“00” | Equal splitting: every frequency layer to be measured within MG is treated equally
“01” | 25% for intra: 25% of MG occasions are used/shared by intra-frequency measurements, and remaining 75% of MG occasions are used/shared by inter-frequency measurements
“10” | 50% for intra: 50% of MG occasions are used/shared by intra-frequency measurements, and remaining 50% of MG occasions are used/shared by inter-frequency measurements
“11” | 75% for intra: 75% of MG occasions are used/shared by intra-frequency measurements, and remaining 25% of MG occasions are used/shared by inter-frequency measurements

## Slide 3: Background
For the sharing of per UE gap or per FR gap for FR1 among NR intra-freq, NR inter-freq, LTE inter-freq and other inter-RAT measurements,
  If we apply the same definition of gap sharing schemes as FR2 gap case, all inter-frequency/RAT frequency layers will be equally treated in any of gap sharing scheme (e.g., in case of “01”:25% for intra, remaining 75% of MG occasions are used and shared by NR inter-frequency, LTE inter-frequency and other RATs measurements).
  Especially for EN-DC operation, LTE inter-frequency measurement (for inter-freq HO) should be prioritized than other inter-frequency measurements (NR and other RATs) in some case.

## Slide 4: Proposal
RAN4 defines separate tables for gap sharing scheme definitions between per UE/FR1 gap case and per FR2 gap case
  For the table of gap sharing scheme definitions in case of per UE gap and per FR1 gap, RAN4 down-selects from two alternatives shown in following slides in RAN4#88

## Slide 5: Proposal
Alt.1: Apply following table in all cases with per UE gap or per FR1 gap
Gap sharing scheme | Definition
“00” | Equal splitting: every frequency layer to be measured within MG is treated equally
“01” | [50]% for LTE inter-freq: [50]% of MG occasions are used/shared by LTE inter-frequency measurements, and remaining [50]% of MG occasions are used/shared by NR intra-frequency measurements and inter-frequency measurements including NR and other RATs (except LTE)
“10” | 50% for intra: 50% of MG occasions are used/shared by intra-frequency measurements, and remaining 50% of MG occasions are used/shared by inter-frequency measurements including NR, LTE and other RATs
“11” | 75% for intra: 75% of MG occasions are used/shared by intra-frequency measurements, and remaining 25% of MG occasions are used/shared by inter-frequency measurements including NR, LTE and other RATs

## Slide 6: Proposal
Alt.2: Apply Alt.1 table in case of EN-DC operation (i.e., LTE PCell case) with per UE gap or per FR1 gap, and apply following table in case of other operations (i.e., NR PCell case) with per UE gap or per FR1 gap
Gap sharing scheme | Definition
“00” | Equal splitting: every frequency layer to be measured within MG is treated equally
“01” | 25% for intra: 25% of MG occasions are used/shared by intra-frequency measurements, and remaining 75% of MG occasions are used/shared by inter-frequency measurements including NR, LTE and other RATs
“10” | 50% for intra: 50% of MG occasions are used/shared by intra-frequency measurements, and remaining 50% of MG occasions are used/shared by inter-frequency measurements including NR, LTE and other RATs
“11” | 75% for intra: 75% of MG occasions are used/shared by intra-frequency measurements, and remaining 25% of MG occasions are used/shared by inter-frequency measurements including NR, LTE and other RATs