## Slide 1: Summary of operators input on the TDD patterns for NR UE performance tests in Rel-15
Ericsson, Verizon, AT&T, CMCC, NTT Docomo, KDDI
3GPP TSG-RAN WG4 Meeting #AH201807 Montreal, Canada, 27 Nov - 1 Dec 2017
Agenda Item: 5.4.1.3
R4-1809555

## Slide 2: Agreed work plan
The work plan for UE performance WI was agreed in R4-1808029.
  Phase 0: Overall test scope, generic common test set-up and channel modelling, specification skeleton
  Phase 1: Completion 1st bullet of test cases (RAN4 July Ad-hoc, RAN4#88)
    Demod:
      PDSCH: Normal test cases with single carrier
      PDCCH
    CSI: CQI (static), PMI, RI test cases
  Phase 2: Completion 2nd bullet of test cases (RAN4#88bis, RAN4#89)
    Demod:
      PDSCH: SDR test, CA/DC/SUL test cases if any
      PBCH if any
    CSI: CQI (fading), L1-RSRP, CRI test cases if any

## Slide 3: Background
Different operators/countries/regions have different planning and considerations on TDD patterns for different frequency bands.
The TDD config for the test set-up is still open for UE performance tests except the FR1 15kHz was agreed as following with the purpose to align the LTE config#2
  FR1:
    15 kHz: DDDSU(aligned with LTE config#2 with 5ms periodicity)
      S = 12D+1Gp+1U
The purpose of UE performance tests should reflect the practical networks based on actual deployment from operators.
In this document summarizes the preference from different operators for different SCS and FR with represents present in this AH meeting.

## Slide 4: FR1
30kHz
Operators | First prior | Second prior
DCM | 7D1S2U, S = 6D:4G:4U | SU, S=12D:2G
CMCC | DDDSUDDSUU, [S1=10D:4G], [S2= 10D:4G] | DDSU, [S = 10D:4G]
Orange | DDDSU, S=10D:2G:2U | 7D1S2U, S = TBD

## Slide 5: FR2
60kHz
120kHz
Operators | First prior | Second prior
DCM | DDDSU, S=10D:2G:2U | DSUU, S=12D:2G
AT&T, Verizon | DDSU, S=11D+3G | 
Operators | First prior
AT&T, Verizon | DDSU, S=11D+3G

## Slide 6: WF for TDD patterns for NR UE performance tests in Rel-15
The UL-DL configurations in the previous two slides should be specified when defining the NR UE PDSCH demodulation performance requirements
  No more UL-DL configuration will be considered for first priority
How to apply the UL-DL configuration to each demodulation performance requirement needs further discussion considering the following approaches
  Alternative 1: Equally splitting the test cases with respect to the UL-DL configurations in Slide #4 and #5.
    Supported by Ericsson, Verizon, AT&T, CMCC, NTT Docomo, KDDI
  Alternative 2: Decide one default configuration for each SCS and define the performance requirements with the default configurations except for a limited number of test cases which will cover all the UL-DL configurations in Slide #4 and #5.
    Supported by Intel, Huawei, HiSilicon, Samsung, Qualcomm
For CSI, only one TDD UL-DL configuration will be specified for each SCS.