## Slide 1: Proposals on TRMS framework
CATR
3GPP RAN4 Meeting MIMO OTA ad-hoc R4-1706404
Qingdao, China, 29-30 June, 2017
Agenda item: 3.1.2
Document for: Approval

## Slide 2: Background
The MIMO WI extension was approved in the RAN plenary meeting, and the remaining task is “Requirements, tolerance, and MU package for the device types and bands listed in the WID”
A framework need to be approved to speed up the MIMO WI progress (only 2 meetings in this WI)
6 bands were approved as the PS1 in performance activity
Aligned MIMO OTA labs could share measurement results into TRMS data pool
  Performance set 1 (PS1) is
    TDD: 41, 38
    FDD Low: 20, 13
    FDD High: 3, 7

## Slide 3: Proposals (1/2)
P1: MIMO OTA TRMS requirements are derived from measurement results of real and commercial devices
P2: The 6 bands listed in PS1 should have high priority
P3: For a given frequency band, the requirement is defined based on the available data (≥15 samples), joint band passing rate shall not be included
P4: The following percentiles shall be picked from the overall TRMS CDFs:
  For TRMS at 70%TP: 80th and 90th percentiles of the CDF of TRMSaverage,70
  For TRMS at 95%TP: 80th and 90th percentiles of the CDF of TRMSaverage,95
MIMO OTA TRMS requirements should be defined as described below:

## Slide 4: Proposals (2/2)
P5: If measurements are not provided for some of the bands in PS1, the WI shall focus on those bands for which data is available and sufficient
P6: the number of supporting bands should be provided at the initial state to avoid the situation like as LTE TRP/TRS
P7: requirement values of TRMS limits will be defined considering agreed percentiles (80% or 90%)
P8: at RAN4#84 aim is to agree TRMS requirements at least for bands in PS1 if data is available
MIMO OTA TRMS requirements should be defined as described below: