## Slide 1: WF on ACLR and ACS for sub-6GHz
Huawei, Hisilicon, China telecom,Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting NR #2
Qingdao, China, 27 - 29 June, 2017
Agenda Item: 3.2.5
R4-1706953

## Slide 2: Background
Contributions have been discussed in NR#2 on sub-6GHz NR BS ACLR and ACS :
  [1] R4-1706684 NR BS ACLR requirements below 6 GHz Huawei, HiSilicon
  [2] R4-1706685 NR BS ACS requirements below 6 GHz Huawei, HiSilicon
  [3] R4-1706825 Wideband ACLR requirement at sub-6GHz ZTE Corporation
  [4] R4-1706582 Discussion on ACLR and ACS for sub-6GHz China Telecom
  [5] R4-1706609 Discussion on ACLR and ACS for sub-6GHz NR coexistence study China Unicom
  [6] R4-1706564 Proposals on below 6GHz NR BS ACLR and ACS Nokia, Alcatel-Lucent Shanghai Bell
  [7] R4-1706661 BS ACLR for below 6GHz NTT DOCOMO, INC.

## Slide 3: Way forward on BS (conducted) ACLR
For wanted channel bandwidth up to 20MHz.
  For bands defined also for E-UTRA
    Specify BS 45 dB ACLR conducted requirement for 5MHz adjacent channel bandwidth only.
For wanted channel bandwidth larger than 20MHz.
  ACLR value
    Adopt the 45dB ACLR1 and ACLR2 to all NR BS classes
  The adjacent channel has the same channel bandwidth as the transmitted carrier.
  For bands defined also for UTRA
    the adjacent channel bandwidth is the corresponding UTRA (FDD or TDD) channel bandwidth.
  For bands defined also for E-UTRA
    Specify BS 45 dB ACLR for 5MHz adjacent channel bandwidth.
    Specify BS 45 dB ACLR for 20MHz adjacent channel bandwidth is FFS.

## Slide 4: Way forward on BS (conducted) ACS
Adopt 46dB ACS to all NR BS.
  FFS on adjacent channel bandwidth
    Option1: The adjacent channel bandwidth is the same as the bandwidth of the wanted signal.
    Option 2: The same number of RB with wanted signal will be used for adjacent interfering signal.