## Slide 1: WF on Mixed Numerologies Requirements
Intel Corporation, Huawei, Ericsson, Nokia
3GPP TSG-RAN WG4 Meeting NR #2 Qingdao, China, 27 - 29 June, 2017
Agenda Item: 3.2.4
R4-1706505

## Slide 2: Background
RAN4 #83 agreements (R4-1706320)
  RAN4 will study the in-band requirement for SS and data channel only if SS and data use different numerologies
    It is possible we may not have requirements on data and SS with different numerology, even though different numerology on data and SS is supported.
  FDM’ed mixed numerologies for downlink and uplink data channel from BS perspective can be supported without additional in-band RF requirements compared to single numerology.
    UE shall be able to TX and RX with one of these numerologies.
    Whether or not mixed numerologies operation using FDM is supported from a UE point of view is FFS

## Slide 3: Background
Mixed Numerologies FDM operation use cases
  Use Case #1: Data and Data mixed numerology FDM
    FDM’ed transmission or reception of physical channels (e.g. NR-PDSCH, NR-PDCCH, NR-PUSCH, NR-PUCCH) with different numerologies at the same instance in DL or UL
  Use Case #2: Data and SS/PBCH mixed numerology FDM
    FDM’ed transmission or reception of SS/PBCH and other physical channels (e.g. NR-PDSCH, NR-PDCCH) with different numerologies in DL

## Slide 4: Way Forward
Case 1 Data/Data mixed numerology FDM requirements
  UE requirements
    Case 1 mixed numerology FDM can be supported without additional UE in-band RF requirements compared to single numerology (e.g. via using inter-numerology guard bands)
    Do not define in-band UE RF requirements for Case 1 mixed numerology FDM in Rel-15
    FFS if any additional mixed numerologies requirements need to be introduced in future releases
  Note: BS requirements are based on R4-1706320 (i.e. no BS requirements)

## Slide 5: Way Forward
Case 2 Data/SS mixed numerology FDM requirements
  Companies views in NR#2 meeting
    View 1: Do not define dedicated RF requirements for Data/SS mixed numerology use case
    View 2: Develop Rel-15 UE requirements for the mixed numerology in-band case where UE receives data and SS/PBCH
      UE receiver intra-band RF requirements
      UE intra-band neighbour cell identification requirements
  Way forwards
    FFS if BS or UE requirements for Data/SS mixed numerology use case are needed. Companies are encouraged to bring further inputs on
      Feasibility of Case 2 mixed numerologies FDM operation from RAN1 design perspective
      Impact on Data channels performance due to mixed numerologies FDM operation
      Impact on SS/PBCH performance due to mixed numerologies FDM operation
      Target BS and UE requirements (e.g. BS RF, UE RF, RRM, UE demodulation)

## Slide 6: Way Forward
Mixed Numerologies Support at UE
  Observations
    Support of FDM of different numerologies transmission or reception leads to increased UE implementation complexity which depends on the number of different simultaneously supported numerologies.
  Case 1: Data/Data mixed numerology FDM
    RAN4 working assumption: Rel-15 NR UE is not mandated to support simultaneous DL reception or UL transmission of multiple FDM’ed physical channels (e.g. NR-PDSCH, NR-PDCCH, NR-PUSCH, NR-PUCCH) with different numerologies at the same time instance.
    Send LS to RAN1/2 in RAN4 #84 to confirm RAN4 working assumption