## Slide 1: Way forward on Unwanted Emission masks for sub-6 GHz
Agenda Item: 3.4.3.2
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 #83 Tdoc R4-1706965
Hangzhou, China, 15 – 19 May, 2017

## Slide 2: Background
The following WF was agreed at RAN4#82bis:
  ΔfUEM =40 MHz for NR bands wider than 100 MHz as baseline for the boundary between UEM and spurious emission( for both Cat A and Cat B );
  The same emission levels for LTE should be used with frequency range (FDL_low– ΔfUEM) ~ (FDL_high+ΔfUEM)
In addition, it was agreed in [4] that ΔfUEM =40 MHz should be applied for bands equal to and wider than 100 MHz.
Several proposals for UEM tables based on the WF were given in [1], [2], [3] and [5]. The Way-Forward is based on the tables proposed and discussed in the BS NR Unwanted Emissions AH meeting.

## Slide 3: Way-forward Agreement
The following variations for the Unwanted Emissions Mask (UEM) tables should be used for sub-6 GHz:
  BS classes
  Category of emission (A/B)
  Frequency range (above/below 1 GHz)
  Power levels (for some BS classes)
The following applies in addition:
  The same tables, but with different Δfmax, will be used for ΔfUEM =10 MHz and ΔfUEM =40 MHz.
  There will be no Options for Category B limits (only LTE Option 1)
  For bands narrower than 100 MHz, ΔfUEM should be further studied .

## Slide 4: References
[1] R4-1706553, "On sub 6GHz NR BS UEM requirement " (ZTE Corporation).
[2] R4-1706643, "NR BS unwanted emission mask for sub-6 GHz" (Ericsson).
[3] R4-1706842, "NR BS Unwanted emission mask for below 6 GHz" (Nokia, Alcatel-Lucent Shanghai Bell).
[4] R4-1706843, "On NR BS boundary between UEM and spurious emission below 6 GHz" (Nokia, Alcatel-Lucent Shanghai Bell).
[5] R4-1706888, "TP to draft TS 38.104: Conducted Tx spurious requirements for NR BS, Range 1" (Huawei, HiSilicon).
[6] R4-1706959, "BS RF evening ad-hoc MoM" (Ericsson).