## Slide 1: WF on unwanted spatial emissions for NR
CMCC
R4-1706972
Agenda : 3.4.2
Document for: Approval
3GPP TSG-RAN WG4 Meeting NR#2
Qingdao, China, June 27th-29th, 2017

## Slide 2: Background
  In order to guarantee the system performance, some declarations related to unwanted spatial emissions should be included in the scope of RAN4 specifications for 5G NR BS in Rel-15.
  In RAN4-NR#2 meeting (June, 2017), companies encourage to provide the views which is best option(R4-1706158), one declaration option should be selected from the three options for unwanted spatial emissions:
      Option1: SLSR and FBR should be included as declarations for 5G NR BS in Rel-15.
      Option2: Side lobe level and front to back ratio potential requirements can be combined into a “emissions spatial mask” declaration
      Option3: Declared The total power that is radiated outside of the 3dB beamwidth within the context of the NR declarations (assuming similar declarations to AAS with this addition)

## Slide 3: Proposal for option 1
Option1: SLSR and FBR should be included as declarations for 5G NR BS in Rel-15
The declaration for Maximum sidelobe direction set, Maximum sidelobe EIRP, Maximum rearward radiation direction set and Maximum rearward radiation EIRP can be defined as:
Declaration identifier | Declaration | Description
D9.xx | Maximum sidelobe direction set | The direction set where the maximum sidelobe EIRP is found.
D9.xx | Maximum sidelobe EIRP | The EIRP at Maximum sidelobe direction set.
D9.xx | Maximum rearward radiation direction set | The direction set where the maximum rearward radiation EIRP is found.
D9.xx | Maximum rearward radiation EIRP | The EIRP at Maximum rearward radiation direction set.

## Slide 4: Proposal for option 2
    Option2: Side lobe level and front to back ratio potential requirements can be combined into a “emissions spatial mask” declaration
    The declaration for option 2 is shown as follows:
    The declaration is made for the widest available cell size provided by the BS
Out of cell directions set | The set of directions that lie outside of the wanted cell
Out of cell power level | the mean radiated power outside of the wanted cell

## Slide 5: Proposal for option 3
    Option3: Declared The total power that is radiated outside of the 3dB beamwidth within the context of the NR declarations (assuming similar declarations to AAS with this addition)
    The declaration of option3 is out of beam power
Out of beam power | The mean power that is radiated outside of the 3dB beamwidth. Declared for every beam identified in D9.3.

## Slide 6: Agreements
  Companies encourage to provide the views which is best option. Other options are not precluded.
In RAN4#84 meeting( Aug, 2017 ), whether to introduce the unwanted spatial emission declaration will be decided. If the unwanted spatial emission declaration is introduced, one of options related to unwanted spatial emissions should be selected for 5G NR BS in Rel-15
A note will be added to capture that radiated power outside of the beam/cell is not the only factors which is relate to system performance and for some types of MIMO/beamforming, minimizing radiation in other directions may not maximize throughput performance
  The specific wording for the note shold be discussed further

## Slide 7: References
  [1] R4-1706158 WF on new BS requirements NTT DOCOMO, INC., CMCC
  [2] R4-1706554 Proposal on new BS requirements for NR CMCC
  [3] R4-1706750 Declaration of out of beam emissions Ericsson
  [4] R4-1706595 Discussion on unwanted spatial emissions for NR CATT
  [5] R4-1706638 Discussion on side lobe level and front to back ratio NEC
  [6] R4-1706644 On new BS requirements Nokia