## Slide 1: Way forward for NR measurement gaps
Ericsson, …
R4-179889

## Slide 2: Measurement gap pattern
Background : Gaps with MGL=6ms and MGRP=40ms,80ms and 160ms have been agreed already by RAN4 for NSA and SA NR measurements. LTE measurement requirements with MGRP=160ms will not be specified.
Additional shorter MGRP and/or MGL can be considered
  Candidate MGL=[3,4,5]ms
  Candidate MGRP=[20]ms
  Other MGRP and ML is not precluded
  Not to add the additional shorter MGRP and/or MGL is also an option
Final selection of MGL and MGRP is expected in RAN4#84bis
  Shorter MGL can be applicable to NSA, SA or both
  Shorter MGL can be applicable to sub 6GHz, mm-wave or both
  Shorter MGRP can be applicable to NSA, SA or both
  Shorter MGRP can be applicable to sub 6HGz, mm-wave or both
Interested companies should provide further details such as the advantage/disadvantages for shorter ML/MGRP, operation of LTE measurements with shorter MGL/MGRP (if requirements for LTE measurement will be specified), considerations on whether shorter MGL/MGRP applies to SA, NSA or both, considerations on whether shorter MGL/MGRP applies to sub 6GHz, mm-wave or both. Other analysis is not precluded
RAN2 needs to be informed of RAN4 findings on measurement gap pattern to complete their work
Notes: Huawei: Prefer MGL and MGRP FFS. Not list 3,4,5. We do not limit to three values. We are not sure whether 20ms is needed.
ZTE: RAN1 just made the agreement. Burst duration is 1 ms and 5ms. 3, 6MGL should be supported.
Intel: The corresponding wording should be revised. Considering the timeline, without significant benefit on other MGL, we would like to postpone the related discussion.
Ericsson: We list the proposals from companies’contributions. I can revised the wording.
Nokia:

## Slide 3: Need for intra-frequency measurement gap
It was agreed (R4-1707424) that there are 3 categories of measurement
  Intra-frequency measurement without measurement gap
  Intra-frequency measurement with measurement gap
  Inter-frequency measurement
Corresponding definitions of intra and interfrequency measurement were also agreed
Following use cases are agreed for measurement gap from RAN4 requirement point of view
  To enable UE to perform intrafrequency measurement when the SSB to be measured is not within the active bandwidth part
  To enable UE perform to RX beamforming in a different direction than the serving cell
  FFS for the use cases related to:
    To enable UE to perform intrafrequency measurement using a different sub carrier spacing than the serving cell PDCCH/PDSCH
Interested companies are invited to analyze
  The need for measurement gaps for the additional use cases
  Any corresponding impacts such as UE capabilities to allow the gNB to correctly configure measurement gaps as needed
  Switching times to be assumed by RAN4 for each of the measurement gap use cases
The target is to complete the analysis by RAN4#84bis
RAN2 needs to be informed of any additional UE capabilities which may be necessary
Notes: Nokia: Clarify the third bullet. Does it not mean that network does not provide the gap to the UE with capability of dual RF chains.
Huawei: delete the third bullet
Intel: In previous WF, we discussed the issue about the gap. For the first bullet, we proposed to replace the sub-bullet. For the fourth bullet, we captured the three bullets in my WF. Based on the discussion, I do not see too much different opinions. We should try to conclude in this meeting.
Ericsson for the third bullet, if we can agree them in this meeting, we are OK. It is related to some detailed work, e.g., switching time.
Intel: the first sub-bullet was agreed in the previous meeting. The last two are new and we think that we should introduce them.

## Slide 4: Measurement of multiple frequency layers with gap
Gap design in NR needs to support measurement of intrafrequency layers (for cases where gap is needed) and multiple interfrequency layers
RAN4 should decide the approach in RAN4#84bis
  Option 1 : NW will configure a single uniform periodic measurement gap pattern to cover the union of SMTC of different frequency layers
  Option 2 : NW will configure multiple measurement gap patterns to cover SMTC of different frequency layers.
    Option 2a : Gap pattern per frequency layer
    Option 2b: Gap pattern per SMTC group
    Option 2c: Gap pattern per frequency range (eg. sub 6Ghz, mm-wave)
  Option 3 : NW will configure a single non-uniform periodic measurement gap pattern to cover the SMTC of different frequency layers
  Option 4 : Other option is not precluded
RAN2 needs to be informed of RAN4 findings on measurement gap for multiple frequency layers to complete their work
RAN4 will define suitable requirements for multiple layer monitoring using gaps (intra and inter) based on the outcome