## Slide 1: WF on interruption on NSA operation
Huawei, HiSilicon, […]
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3 R4-1709901
Nagoya, Japan, 18 - 21 Sep, 2017
Agenda: 3.5.5

## Slide 2: Background
In this WF, it is assumed the following scenario
E-UTRA-NR DC where the E-UTRA is the master (Option 3/3a/3x in TR 38.801 section 10.1.2)
PCell and SCell in MCG belongs to LTE
PSCell and SCell in SCG belongs to NR

## Slide 3: Scenario for study (for example, other not precluded)
Type of NSA operation | Victim | Aggressive | Define interruption requirement or not
PSCell is added or released | PCell SCell in MCG (No SCell in SCG in this case) | PSCell | Yes
SCell in either MCG or SCG is added or released | PCell and activated SCell in MCG PSCell and activated SCell in SCG | SCell in MCG SCell in SCG | Yes
SCell in either MCG or SCG is activated or deactivated | PCell and activated SCell in MCG PSCell and activated SCell in SCG | SCell in MCG SCell in SCG | Yes
measurements on SCC with deactivated SCell in either MCG or SCG | PCell and activated SCell in MCG PSCell and activated SCell in SCG | SCell in MCG SCell in SCG | FFS maximum interruption length requirement FFS requirement of probability of missed ACK/NACK
transitions between active and non-active during DRX | PCell and activated SCell in MCG PSCell and activated SCell in SCG | PSCell PCell | FFS maximum interruption length requirement FFS requirement of probability of missed ACK/NACK
transitions from non-DRX to DRX | PCell and activated SCell in MCG PSCell and activated SCell in SCG | PSCell PCell | FFS

## Slide 4: Interruption on NSA operation
Definition of Synchronous asynchronous DC:
  Whether to introduce synchronous dual connectivity definition and if introducing FFS related requirement/definition.
  Whether to introduce asynchronous dual connectivity and if introducing FFS related requirement/definition.
UE architecture:
  FFS LTE and sub 6GHz NR receivers may be implemented on the same RFIC
  FFS LTE and mm wave NR receivers will not be implemented on the same RFIC
Interruption requirement related to NR SCS:
  Whether and how to scale interruption due to different SCS if victim in MCG(LTE) and aggressive in SCG(NR)
  Whether and how to scale interruption due to different SCS if victim in SCG(NR) and aggressive in MCG(LTE)
  Whether and how to scale interruption due to different SCS if victim in SCG(e.g. SCell) and aggressive in SCG(e.g. PSCell)
  Unit of interruption length caused by NSA operation
      in ms (subframe)
      In symbol or slot
      Other
CR structure:
All interruption requirements whose victim is LTE are defined in TS36.133. (Only for example)
All interruption requirements whose victim is NR are defined in TS38.133. (Only for example)