## Slide 1: WF on LTE/NR UL subcarrier alignment
Huawei, HiSilicon, China Mobile, vivo, China Telecom, MediaTek, Spreadtrum, Deutsche Telekom, Orange, Vodafone, Bell Mobility, China Unicom

## Slide 2: Background
It was agreed that LTE/NR UL subcarrier alignment is to be specified by Dec 2017 in RP-172104, “Way forward on UL sharing aspects” at RAN#77.
To achieve LTE/NR subcarrier alignment, the following options are possible
  Option 1: Base band shift with 7.5kHz shift, without requiring LO frequency retuning, applicable to both shared and independent RFs
  Option 2: Digital rotator with 7.5kHz, without requiring LO frequency retuning , applicable to both shared and independent RFs
  Option 3: RF shift with independent RFs, without requiring LO frequency retuning
  Option 4: RF shift with shared RFs, requiring LO frequency retuning

## Slide 3: Option 1: BB shift
Tx HF
LTE BB ASIC
NR BB with 7.5 kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
Tx LF
3.5 GHz
1.8 GHz
PLL
PLL
PA@1.8GHz
PA@3.5GHz
LTE
RF IC
Tx LF
Tx HF
LTE
BB ASIC
NR BB with 7.5kHz shift
ASIC
LTE
Modem
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
RF@
1.8GHz
DAC
PA@1.8GHz
PA@3.5GHz
NR
Modem
NR
RF IC
RF other band
…
BB shift is applicable to implementations with either shared or independent RF for LTE/NR at the shared carrier
BB shift does not require LO frequency retuning and minimizes the LTE/NR switch time

## Slide 4: Option 2: Digital rotator
LTE
RF IC
Tx LF
Tx HF
LTE
BB ASIC
NR BB
w/o 7.5kHz shift
ASIC
LTE
Modem
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
RF@
1.8GHz
DAC
PA@1.8GHz
PA@3.5GHz
NR
Modem
NR
RF IC
RF other band
…
Tx HF
LTE BB ASIC
NR BB
w/o 7.5 kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
Switch
DAC
RF@
3.5 GHz
DAC
Tx LF
3.5 GHz
1.8 GHz
PLL
PLL
PA@1.8GHz
PA@3.5GHz
7.5kHz digital rotator
7.5kHz digital rotator
Digital rotator is applicable to implementations with either shared or independent RF for LTE/NR at the shared carrier
Digital rotator does not require LO frequency retuning and minimizes the LTE/NR switch time

## Slide 5: Option 3: RF shift with independent RFs
RF shift with independent RFs does not require LO frequency retuning and minimizes the LTE/NR switch time
Tx HF
LTE BB ASIC
NR BB w/o 7.5kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
RF@
1.8 GHz
DAC
RF@
3.5 GHz
DAC
Tx LF
PA@1.8GHz
PA@3.5GHz
RF@
1.8000075 GHz
DAC
PA@1.8GHz
+7.5kHz

## Slide 6: Option 4: RF shift with shared RFs
RF shift with shared RFs requires LO frequency retuning and degrades the system performance
Tx HF
LTE BB ASIC
NR BB w/o 7.5kHz shift ASIC
LTE/NR
Modem
LTE/NR
RF IC
DAC
RF@
3.5 GHz
DAC
Tx LF
PA@3.5GHz
RF @ 1.8GHz or 1.8000075 GHz
PA@ 1.8GHz or 1.8GHz +7.5kHz

## Slide 7: WF
For UL sharing from both network and UE perspective, UL LTE/NR subcarrier alignment is achieved without LO frequency retuning, to minimize the LTE/NR switching time
Define the corresponding RAN4 requirement(s)
Inform RAN1 and RAN2 about the above RAN4 agreement