## Slide 1: WF on wideband operation for both gNB/UE aspects
LG Electronics, ZTE, Intel, Samsung, Huawei, MediaTek, Nokia
R4-1709933
3GPP TSG-RAN WG4 NR AH #3 Meeting
Nagoya, Japan, September 18 -21, 2017
Agenda: 3.2.1.2

## Slide 2: Background (1)
LS from RAN1
  R1-1706615 LS on Wideband Operating Options
WF in RAN4 #84
  R4-1708849 WF on Further clarification on wideband operation, LGE, MediaTek, Huawei,
  Nokia and ZTE
  R4-1708851 WF on spectrum utilization in wideband operation, ZTE
Contributions in NR AH #3
  R4-1709579 Further clarification for Wideband operation of NR UE LGE
  R4-1709346 Further discussion on wideband operation Samsung
  R4-1709744 UE spectrum utilization in wideband operation Nokia
  R4-1709385 Further consideration on spectrum utilization in wideband operation ZTE
  R4-1709722 Wideband and CA Operation for NR Qualcomm
  R4-1709407 On UE bandwidth support in NR Intel
In RAN4 NR AH #3 meeting, RAN4 has been discussed in terms of the related UE RF requirements, UE capability and gNB impact.

## Slide 3
Definition of wideband operation
  RAN1 Agreements of Wideband operation (R1-1706615)
    A gNB can operate simultaneously as wideband CC for some UEs and as a set of intra-band contiguous CCs with CA for other UEs.
  One or multiple bandwidth part configurations for each component carrier can be semi-statically signaled to a UE
    The bandwidth of a bandwidth part equals to or is smaller than the maximal bandwidth capability supported by a UE (RAN1 #88 BIS agreements)
    Configuration of a bandwidth part may include the following properties (RAN1 #89 agreement)
      Numerology (SCS, CP type)
      Frequency location (e.g. center frequency)
      Bandwidth (e.g. number of PRBs)
    Primary focus is to complete the single active bandwidth part case (RAN1 AH #2 agreement)
    In Rel-15, for a UE, there is at most one active DL BWP and at most one active UL BWP at a given time for a serving cell (RAN1 AH #3 agreement)
Background (2)

## Slide 4
Scenarios of wideband operation for FR1 and FR2
  In UE aspect, no additional UE requirements in rel-15
    Single carrier UE operation within a serving cell
      UE requirement is the same as single carrier ones.
    Multiple active BWPs within a serving cell
      Deprioritized scenario per RAN1 decision
    Whether new requirements are needed can be discussed based on RAN1 agreements
  In gNB aspect, no additional gNB requirements in rel-15
Aggregated carrier UE operation across multiple BS CCs
  LTE Intra-band contiguous CA requirements are a starting point for NR requirements
Way Forward (1)

## Slide 5
Spectrum utilization for wideband operation
  In gNB aspect, SU in the wideband operation was agreed at last RAN4 meeting as below :
    Spectrum utilization should be defined as the same as single channel bandwidth regardless of how UE supports the wideband
  In UE aspect, SU follow as same the SU of single CC of each operating NR Band when RAN4 only consider single active BWP within a serving cell in rel-15.
    SU of aggregated CHBW w/ multiple active BWPs will be discussed in future based on RAN1 agreements.
Spectrum utilization of intra-band contiguous carrier aggregation is FFS.
Way Forward (2)

## Slide 6
gNB
Max. supported CBW is 200MHz for All UEs
Configured BWP of UE1, UE4, UE5: 100MHz
Configured BWP of UE2, UE3 : 200MHz
Configured BWP of UE6 ~UE9: 50MHz
RAN4 need to specify UE RF requirements for only UE1 Case for wideband operation
(100M+100M wideband operation)
Other UE follow single carrier RF requirements
UEs
CC1 (400MHz)
CC2 (400MHz)
CC3 (200MHz)
1GHz
UE6 (50MHz)
UE1 (100MHz)
UE3
(200MHz)
UE1 (100MHz)
UE4 (100MHz)
UE5 (100MHz)
UE2
(200MHz)
UE7 (50MHz)
UE8 (50MHz)
UE9 (50MHz)
UE wideband operation
RAN1 agreement for activated BWP is single per CC
  Primary focus is to complete the single active bandwidth part case a serving cell
  So, UE RF requirements is not need to define to support multiple active BWPs.
Information: Deprioritized scenario in rel-15

## Slide 7
gNB
UEs
UEs
CC1 (400MHz)
CC2 (400MHz)
CC3 (200MHz)
1GHz
UE2 (50MHz)
UE1 (400MHz)
UE1 (400MHz)
UE3 (50MHz)
UE4 (50MHz)
UE5 (50MHz)
UE1 (200MHz)
UE1 (400MHz)
UE1 (400MHz)
Or
Base on RAN1 agreement, activated BWP is single per CC for UE
RAN4 focus on UE RF requirements for Intra-band contiguous CA in rel-15
Information: Intra-band contiguous CA
* Max. supported CBW of UE1 is 400MHz, just shown here for example