## Slide 1: WF on Sync Raster for NR
Qualcomm Incorporated, Vodafone, Ericsson, Dish, T-Mobile USA, Intel, Oppo, Orange, Verizon
3GPP TSG-RAN WG4 RAN4 AH#3
Nagoya, Japan, September 18th-21st, 2017
R4-1709936
Document for: Approval

## Slide 2: Background
RAN1 agreed SS block design that has 24RBs(PSS/SSS block of 12RBs and PBHC of 24RBs)
RAN4 agreed minimum channel bandwidth of 5MHz for most LTE re-farming bands and 50MHz for mmWave bands

## Slide 3: Problems
Based on the agreed spectral utilization values, SS block with 30kHz SCS cannot be used in 5MHz channels
  30kHz SS block SCS cannot be used for initial system acquisition in bands with 5MHz minimum channel bandwidth unless multiple default SS block SCS are assumed
240kHz SS block SCS cannot be used in 50MHz channels
  240kHz SS block SCS cannot be used for initial system acquisition in mmWave bands with 50MHz minimum channel bandwidth unless multiple default SS block SCS are assumed
The number of entries for the synchronization raster used for initial system acquisition depends on the SS block bandwidth and the minimum channel bandwidth defined in a band
  The current SS block design leads to a very large number of sync raster entries making it impractical for UEs to search all possible entries
  The acquisition delay or search complexity will increase if the UE has to search for multiple SS block SCS hypothesis

## Slide 4: Possible solutions
Increasing the minimum channel bandwidth in which initial system acquisition is needed
  Not a practical solution because spectrum holdings are different for different operators
Decreasing PBCH bandwidth
  Leads to significant down-selection of the sync raster for any SS block SCS
  If PBCH is reduced to 12RBs, the SS block for higher numerologies(240kHz) can be used in the minimum channel bandwidth so there would not be any need for multiple search hypothesis
Allowing multiple default sync block SCS values per band
  Will increase the initial acquisition time/complexity
  Needs RAN1 decision

## Slide 5: Way Forward
Reducing PBCH bandwidth is the best solution to improving the initial system acquisition performance and to allow the use of 240kHz sync block SCS as the default SCS value in multiple bands. Examples below if PBCH BW is reduced from 24RBs to 12 RBs
  Band n3 (DL 1805MHz-1880MHz)
    15kHz SS block SCS, the number of sync raster entries is reduced from 701 to 84 entries
  Band n66 (DL 2110MHz-2180 MHz)
    with 15kHz SS block SCS, the number is reduced about 8 times (78 entries from 651)
    With 30kHz SS block SCS, the number is reduced about 15 times (39 entries from 601)
    If both SCSs are allowed, the number is reduced about 10 times (117 entries from 1251)
  Band n78 (DL 3.3GHz-3.8 GHz)
    With 30kHz SS block SCS, the number is reduced about 44 times (112 entries from 4901)
Send an LS to RAN1 to ask RAN1 to reconsider the PBCH design and the feasibility and implications of reducing the PBCH bandwidth