## Slide 1: WF on carrier leakage frequency
Huawei
3GPP TSG-RAN WG4 Meeting NR ad-hoc #3 R4-1709935
Nagoya, Japan, 18 - 21 Sep, 2017

## Slide 2: Background
  RAN4 has discussed the carrier frequency, carrier leakage frequency for each sub-carrier spacing in [1] and made some assumptions from RAN4 point of view. These assumptions need further discussion in RAN4.
  RAN4 is working on MPR simulation and has a assumption on the position of carrier leakage (the centre of CBW). MPR simulation results depend on this assumption.

## Slide 3: Way forward
For sub-6GHz
For single carrier, carrier leakage frequency should be specified.
  The specific carrier leakage position in one carrier is FFS
    MPR simulation should also use this position as assumption
  Whether the carrier leakage frequency should be the same for each sub-carrier spacing should be studied and decided.
  Whether the carrier frequency should be the same for each sub-carrier spacing should be studied and decided.
For wideband operation and CA operation, the carrier leakage frequency should be FFS.
For mmWave:
carrier leakage frequency is FFS.

## Slide 4: Reference
[1] R4-1709551, Discussion on DC location, Huawei, HiSilicon

## Slide 5: Annex
RAN1 has made an agreement considering DC sub-carrier:
Handling of transmitter DC subcarrier at the transmitter
  DL
    UE may assume transmit DC subcarrier at the transmitter (gNB) side is modulated i.e., data is neither rate-matched nor punctured.
      Signal quality requirement (e.g., EVM) corresponding to DC subcarriers is up to RAN4.
  UL
    Transmit DC subcarrier at the transmitter (UE) side is modulated i.e., data is neither rate-matched nor punctured.
      Signal quality requirement (e.g., EVM) corresponding to DC subcarriers is up to RAN4.
    The transmitter DC subcarrier at the transmitter (UE) side should avoid collisions at least with DMRS if possible
    The specification should define at least one particular subcarrier as the candidate position of DC subcarrier, e.g., DC subcarrier is located at the boundary of PRBs
    This should be considered in the RS design for NR
    Specify means for the receiver to determine DC subcarrier location
      This involves semi-static signalling from UE and also standard specified DC subcarrier location
      FFS how to determine and how to indicate DC subcarrier location in the case of bandwidth adaptation
Note that above DC subcarrier can be interpreted as DC subcarrier candidate