## Slide 1
WF on Power class for mm Wave
Qualcomm, [Intel], [LGE]
3GPP WG4-NR-AH#3 R4-1710081
18 - 21 Sep, 2017 Nagoya, JP

## Slide 2: Background
mmW UE output power has been discussed in many meetings including this meeting (NR-AH#3 Nagoya)
WF was agreed in RAN4#84 Berlin
  [1] R4-1709146, “WF on power class and CDF for mmWave UEs”, NTT DOCOMO, INC, RAN4#84 Berlin, Aug 2017
WF was to agree Power class definition in next meeting considering below candidates according to the possible RAN1 answer
  Peak EIRP over the sphere with minus tolerance
  EIRP at CDF percentiles with minus tolerance
    [5-20] %
    [50] %
    [80-90] %
  Maximum allowed EIRP such as 43, 55 dBm (FCC limits)
  Maximum allowed TRP will be discussed in the next meeting

## Slide 3: Background on spherical coverage
Spherical coverage requirement is defined as (RAN4#82 Chairmen minutes)
  RAN4 method for describing spherical coverage of RF parameters is CDF where each point represent equal surface area in sphere surrounding the UE.
In Chairman minutes for AH#3 following was agreed
  EIRP for spherical coverage @ somewhere below 50%
Reported %-tiles in submitted papers below 50 % are 5, 10, 20 %-tiles

## Slide 4: Way Forward on spherical coverage
Companies are encouraged to consider following aspects in addition to the parameters listed in [1]
  Number or antenna arrays and placement options with realistic industrial design including diplay and device case material
  Perturbation or distortion of mmWave antenna radiation by the LCD, and gap in-between antenna and housing of the UE)
  Possible usage positions of the UE and relevance of spherical coverage
Decision beteen two %-tile values will be made based on submissions in RAN#84Bis
Assumption is that output power is specified with the waveform and modulation with lowest MPR
  Waveform and modulation is pending for MPR analysis
dBm Value of %-tiles will be discussed in next meeting
  The requirement should be future-proof especially considering current results is only based on simulation result rather than measurement with practical implementation.
Since requirement is only lower limit, no tolerance will be specified
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability

## Slide 5: Background on power class
In chairman minutes for AH#3
  EIRP for PowerClass @100%, or 90% or 50%

## Slide 6: Wayforward on power class
RAN4 will specify a requirement for max EIRP
  Maximum EIRP will have only lower limit i.e. UE will meet the requirement as long as it exceeds the defined limit in to one direction
Value of lower limit for max EIRP will be discussed in next meeting
Assumption is that output power is specified with the waveform and modulation with lowest MPR
  Waveform and modulation is pending for MPR analysis
Since requirement is only lower limit, no tolerance will be specified
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability

## Slide 7: Way forward max allowed EIRP
Max allowed EIRP of 43 dBm is regulatory requirement and does not need to be discussed (agreement allready in R4-1706322, ”WF on mmWave UE output power”, Qualcomm, RAN4#83
RAN4 will specify this limit in 38.101-2
Requirement is valid for all waveform, modulation and conditions

## Slide 8: Way forward on TRP
RAN4 will specify a requirement for TRP
The TRP requirement is only upper limit, so no tolerance will be specified
Value of upper limit for TRP will be discussed in next meeting
Test tolerance, as derived from the test system measurement uncertainty, will be defined based on progress in testability