## Slide 1: WF on BS/UE channel bandwidth definition
R4-1709930

## Slide 2: Proposal: UE Channel bandwidth
UE Channel bandwidth: The RF bandwidth supporting a single E-UTRA NR RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell. The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements.

## Slide 3: Proposal: BS Channel Bandwidth
BS Channel bandwidth: RF bandwidth supporting a single E-UTRA NR RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell.
  NOTE: The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements.
  NOTE: It is possible for the BS to transmit to and/or receive from one or more UE Bandwidth parts that are smaller than or equal to the BS transmission bandwidth configuration, in any part of the BS transmission bandwidth configuration.