## Slide 1
NB-IoT SIG Test Issues
for Discussion
2016.5
CATT, CMCC, TDIA, StarPoint

## Slide 2: SA2 Progress on C-IoT
Progress @ SA2#114 meeting
Attach/TAU Procedure related
CP Optimizations related
Simultaneous support of CP & UP optimizations
Next SA2 meeting is SA2#115 on 23 - 27 May 2016 in Nanjing
Planned completion date: must complete before next SA#72 in June 2016

## Slide 3: Attach/TAU Procedure Related
Introduced the concept the cells advertise support of some C-IoT features in the SIB for the PLMNs it supports. (S2-162051 )
Network features need to be consistent across TAI LIST. (S2-161910)

## Slide 4: CP Optimizations Related
Removes indication of whether Header Compression is supported from Preferred and Supported Network Behaviour and clarifies that the indication of whether the MME successfully obtained Header Compression Configuration parameters or not should be per EPS Bearer ID. (S2-162024)
Clarifies that a UE and MME that support Control Plane CIoT EPS optimisation to send/receive SMS. (S2-162053)
Added support for rate control of Control Plane data (DoNAS). (S2-162054)

## Slide 5: Simultaneous Support of CP & UP Optimizations
Clarify that the UE does not send Release Assistance Indicator when it has S1-U bearers established and the MME ignores any Release Assistance Indicator sent by the UE if the UE has an S1-U connection (either because of a resume or a normal service request).
Only data using 'PDN connections to SCEF' can use CP optimisation after the AS context is established/resumed.
In order for the MME to indicate to the UE that it is allowed to send data for these PDN connections using CP optimisations, even after the DRBs are established, the MME includes a Control Plane Only Indicator in the Session Management Request only for PDN connections with a SCEF.
Add new procedure text for UE initiated Service Request during Data Transport in Control Plane CIoT EPS optimisation.
(S2-162058)

## Slide 6: CT1 Progress on C-IoT
Progress @ CT1#97&Adhoc meeting (discussed and agreed)
EMM and ESM procedure on CIOT Optimization
Draft for piggyback SMS within EMM procedure
Switch between CP and UP
Paging response for MT CIoT data
Support of EMM-REGISTERED without PDN connectivity
CIOT capability indication and negotiation
Link MTU size for non-IP PDN connection
Rate control for CIOT
Working agreement for explicit indication in SIB supporting "attach without PDN connectivity" .
Next CT1 meeting is CT1#98 on 23 - 27 May 2016 in Osaka
Planned completion date: may be postponed to July or September 2016

## Slide 7: EMM & ESM Procedure on CIOT Optimization
  Suspend and resume of the NAS signalling connection for UP solution are added. (CT1#97 C1-162169) (EMM procedure)
  Trigger to resume NAS signalling in EMM procedures is added. (CT1 adhoc meeting C1A160100) (EMM procedure)
  Service Request procedure is enhanced to transfer of data via control plane. DATA SERVICE REQUEST procedure is defined to enable UE to transfer data in EMM-IDLE mode or CP solution. SERVICE ACCEPT message is defined to terminate the Service Request procedure for certain use cases. (CT1#97 C1-162166) (EMM procedure)
  New EPS procedure and ESM DATA TRANSPORT msg are defined to enable transferring small data via the MME when the UE is in EMM-CONNECTED mode. (CT1#97 C1-162325) (ESM procedure)

## Slide 8: Switch between CP and UP
Reuse the TAU procedure with active flag allowing the UE to initiate it while in connected mode so that it’s used as a trigger for the MME to switch from CP to UP CIoT EPS optimization. (CT1 adhoc meeting C1A160122)

## Slide 9: Paging
Paging procedure can trigger the resumption of a NAS signalling connection to the UE. (CT1 adhoc meeting C1A160115)
Paging response for MT CIoT data: (CT1#97 C1-161972)
  Stop T3346 and initiate service request procedure or TAU to respond
  Upon receive paging, CP is not used.
  Stop T3346 and send DATA SERVICE REQUEST to respond
  Upon receive paging, CP is used, without suspend indication.
  Stop T3346 and initiate resume procedure firstly
  Upon receive paging, CP is used, with suspend indication.

## Slide 10: Support of EMM-REGISTERED without PDN Connectivity
If both the UE and the MME support EMM-REGISTERED without PDN connection, the establishment of a default EPS bearer context during the attach procedure is optional. (CT1#97 C1-162308)
Furthermore, the UE and the MME can deactivate the last remaining PDN connection without entering EMM state EMM-DEREGISTERED. (CT1#97 C1-162308)

## Slide 11: C-IoT Capability Indication and Negotiation
If the network supports user plane EPS optimization, it has to also support S1-U data transfer. (CT1#97 C1-162117)
The EPS network feature support IE is enhanced to carry information of support of control-plane CIoT EPS optimization, user-plane EPS optimization, S1-U data transfer, and header compression for control-plane EPS CIoT optimization. (CT1#97 C1-162331)
MME will take the CIoT optimisation support into account when allocating TAI list. (CT1adhoc meeting C1A160098)
If the “active” flag is included by the UE during the TAU and EPS services with CP-CIoT optimization is not used by the UE or the MME, the re-establishment of the corresponding user plane radio bearers is needed for all active EPS bearers. (CT1#97 C1-162126)

## Slide 12: Link MTU Size for Non-IP PDN Connection
Introduce new PCO parameters for link MTU option. And the NW shall use a maximum packet size of at least 128 octets for both uplink and downlink. (CT1adhoc meeting C1A160114)
Add handling to communicate link MTU to the UE during non-IP connection establishment. But how the UE will use the Non-IP Link MTU received is FFS. (CT1adhoc meeting C1A160123)

## Slide 13: Rate Control for CIOT
At the PDN connection establishment, MME can inform the UE about the serving PLMN rate control value and if included, the UE enforces the value. (CT1adhoc meeting C1A160128)

## Slide 14: Working Agreement
CT1 Chairman proposed to use the 3GPP mechanism "working agreement" to secure the progress on C-IOT.
The working agreement is:
  "CT1 has decided that an explicit indication in the SIB of support for "attach without PDN connectivity" by the network, will prevent the UE from having to discover availability of such a feature by using trial and error in Attach request and will facilitate handling when UE moves across tracking areas or changes PLMNs."
This text is published at http://www.3gpp.org/specifications-groups/32-tsg-working-agreements
The vote following the challenge would be done in Osaka.

## Slide 15: Issues Need Further Work
Extensions of NAS timers. (HW thought single multiplier is enough.) (CT1 adhoc meeting C1A160022)
How to configure the NB-IoT UE for NAS signalling low priority and for mo-ExceptionData reporting? (CT1 adhoc meeting C1A160035)
Rate Control for CIoT, CT1 against the APN based rate control that SA2 proposed. (CT1 adhoc meeting C1A160011)
Data Service Request MSG piggy back PDN connectivity request MSG. (postponed to Osaka meeting, CT1 adhoc meeting C1A160033)

## Slide 16: Issues Need Further Work
SMS transfer using CP CIOT optimization need to perfect. (CT1 adhoc meeting C1A160120)
How to notify the network to hold the NAS signalling for further proceeding in the TAU. HW propose to reuse “active flag”. (CT1 adhoc meeting C1A160045)
How the UE will use the Non-IP Link MTU received is FFS. (CT1adhoc meeting C1A160123)
The UE only using EPS services with CP-CIoT EPS optimization shall trigger NAS signalling connection recovery only if a downlink data transmission is expected. (postponed to Osaka meeting, CT1 adhoc meeting C1A160033)

## Slide 17: RAN2 Progress on NB-IoT
NB-IoT running CRs (WG2 Meeting NB-IoT Ad-hoc, 3th – 4th May 2016)
36.300: R2-163218
36.331: R2-163221
36.306: R2-163273
36.304: R2-163244
36.302: R2-163219
36.321: R2-163259
36.322: R2-163216
36.323: R2-163238
Next RAN2 meeting is RAN2#94 on 23 - 27 May 2016 in Nanjing
Planned completion date: June 2016

## Slide 18: New Features on NB-IoT <1>
A new UE category named Category NB1
Support of “attach without PDN connectivity”
Introduce an indication signalled per PLMN in SIB1.
Introduce an indication at connection establishment, to be used at attach, in MSG5.
RRC establishment cause
mt-Access, mo-Signalling, mo-Data, mo-Exception-Data(new).
“emergency” or “delaytolerantaccess” cause values are not applicable to NB-IoT.
Two priority cases for MO data: a) normal reporting ; b) exceptional reporting
mo-Exception-Data
UE shall initiate an RRC connection with cause mo-ExceptionData only to send exception reports. Exception reports can be sent on RRC connections regardless establishment cause value.
UE shall not use an RRC connection established with cause mo-ExceptionData to send other data than exception reports. Remains FFS
Multiple DRBs
UP solution can optionally supports more than 1 DRB, the higher capable UE supports 2 DRBs.

## Slide 19: New Features on NB-IoT <2>
Simultaneous support for CP and UP optimizations
In a RRC connection either “TM PDCP / no PDCP” or “normal PDCP” is used.
Before Security is started we always use no PDCP.
RAN2 will support “TM PDCP / no PDCP” -> “normal PDCP” change in one RRC connetion, but not vice versa.
Confirm that data could be sent over CP and UP within the same RRC connection.
a LCID indication distinguishs when “PDCP-TM / no PDCP” vs “full PDCP” is used for the SRB.
The transmissions with PDCP-TM / no PDCP are done on a separate SRB which is called SRB1bis, and is using the same configuration as SRB1 except for PDCP.
For a UE using the SRB with PDCP-TM / no PDCP, AS security can be activated by a Security Mode Command (which is then sent on SRB1, i.e. with full PDCP)

## Slide 20: New Features on NB-IoT <3>
Multi-PRB （Multi-carrier）
After the successful completion of RRC connection (re)establishment, resume or reconfiguration, if configured, the UE can start to receive NB-PDCCH/NB-PDSCH and/or transmit NB-PUSCH on a non-anchor PRB;
A UE that has been assigned a non-anchor PRB, remains on that PRB throughout RRC_CONNECTED or until transmission of NB-RACH is needed in RRC_CONNECTED or until re-assigned to another PRB.
The RA procedure is performed on an anchor PRB;
The RRC connection (re)establishment/resume procedure is initiated on an anchor PRB. If the UE needs to perform a RA procedure while on the non-anchor carrier (e.g. due to SR or PDCCH order) it goes back to the anchor carrier and stays there throughout RRC_CONNECTED or until re-assigned to another PRB (We may consider the mechanism to go back to the non-anchor PRB after the RA procedure).
for SR, the UE goes back to the anchor, after the RACH, the UE stays on the anchor unless explicitly redirected again.
A UE in RRC_IDLE receives paging on an anchor PRB.

## Slide 21: New Features on NB-IoT <4>
Suspend/Resume Procedure
new RRC message RRCConnectionResumeRequest, RRCConnectionResume, RRCConnectionResumeComplete
Use existing RRC messages RRCConnectionSetupReject as a response to RRCConnectionResumeRequest
It shall be possible that ROHC can continue at resume.
The protocol entities for PDCP and RLC are kept when the RRC connection is suspended, and are re-established at RRC Resume.
MAC is reset at resume.
At reject the UE stays suspended and keeps the stored UE context, or removes the stored UE context and goes to Idle, based on indication in the reject message.
At connection setup the stored UE context is removed and not used.
UE can receive data on DRB after having received and processed RRC resume message.
The UE is not required to be able to receive data on DRB and the RRC resume message in the same TB.
Security is fully resumed on UE side after reception and processing of RRC connection resume message and UL data on DRB(s) can be sent with “message 5”.

## Slide 22: New Features on NB-IoT <5>
Suspend/Resume procedure(2)
Ask SA3 to clarify whether integrity protection and/or ciphering is needed for SRB/DRB configuration/reconfiguration at RRC connection resume.
If SA3 indicates that also SRB/DRB configurations can be present in the RRC resume message then we add that possibility later.
RAN2 assumes that it is up to the NAS layer to choose how to continue after a failure when Resume procedure fails, when the context has been removed in the UE
RAN2 assumes that NAS may choose between establishing the DRB or using CP solution for NB-IoT

## Slide 23: New Features on NB-IoT <6>
Access Control
NB-IOT access barring is specified separately from LTE access control mechanisms.
ab-Enabled in theMasterInformationBlock-NB indicates whether access barring is enabled.
Change of Access Barrring (AB) parameters can occur at any point in time.
SIB14b-nb includes all Access Barrring (AB) parameters.
Both RRCConnectionEstablishment and resume is to AC Barring.
Idle Mode Mobility
The selection criteria S is fulfilled when both Srxlev > 0 AND Squal > 0;
Intra-frequency and inter-frequency cell reselection are both based on ranking based mechanism. Inter-frequency mobility based on priority is not supported;

## Slide 24: Idle Mode
System Infomation
System Information including MIB, SIB1 and SI messages for NB-IoT is following :
  MIB (new indication systemInfoValueTag-r13 & ab-Enabled-r13)
  SIB1-nb
  SIB2-nb
  SIB3-nb
  SIB4-nb
  SIB5-nb
  SIB14-nb(Access barring)
  SIB16-nb
UE can monitor notification about system information update through physical layer control channels, as specified in TS 36.211 if there is no paging record after PDCCH. The system information change indication (1bit for Systeminfomodification and 1bit for systemInfoModification-eDRX) carried in DCI is supported.
Paging
Different transmission repetitions are used for different coverage level;
Use DRX or eDRX

## Slide 25: Random Access Procedure
Only contention-based random access is supported for NB-IoT.
PDCCH order is supported for DL data arrival;
Contention free RACH / dedicated preambles for Handover or other reconfigurations in this release is not supported;
A set of PRACH resources (e.g. time, frequency, and preamble sequences) is provided for each coverage level. The UE selects PRACH resources based on coverage level given by a UE DL measurement, e.g. RSRP;
It should be possible to have different backoff times for different coverage levels. FFS if we Use PRACH period as basic unit for backoff. The backoff time can be caluculated as Backoff Parameter value * PRACH period.
the tone information shall be included in the RAR, in the Random Access Preamble ID field in the MAC PDU subheader.
MSG3 including multi-tone UE capablity indication, multi-PRB UE capablity indication, 2 bits PHR and 4-bit DVI (data volume indication indicates the amount of user data (including SMS) and NAS signalling data volume sent over user plane or control plane)

## Slide 26: MAC
The following MAC layer functions are assumed not supported:
MBMS service;
Semi-Persistent Scheduling;
Dedicated Scheduling request;
Activation / deactivation (definition needs to be further clarified).
BSR
We use NB-IoT specific DVI/PHR for MSG3, and use LTE BSR for non-MSG3 cases.
For NB-IoT a subset of LTE BSR support, the subset is FFS.
Only a Short BSR is supported for NB-IOT (no long BSR).
For NB-IoT all logical channels belong to one LCG that do not need to be configured by RRC. This LCG comprises both SRB and DRB.
A single HARQ process is supported for dedicated transmissions (1 for UL and 1 for DL).
DRX in connected mode is supported, but only long DRX. It is beneficial to enable DRX also for short connections
New MAC Control Element: Data Volume and Power Headroom Report

## Slide 27: RLC
The RLC layer supports the following functions:
Transfer of upper layer PDUs;
Concatenation, segmentation and reassembly of RLC SDUs;
RLC AM is supported for both SRB and DRB. The concerns of power consumption, number of transmissions and complexity should be addressed;
RLC re-segmentation;
RLC re-establishment is supported for the UP solution but is not required for the CP solution (to be clear by RRC);
In-sequence delivery and duplicate detection;
The following RLC layer functions are assumed not supported:
RLC UM is not supported.
Reordering of RLC data PDUs ;

## Slide 28: PDCP
For NB-IoT UE supports Control Plane CIoT EPS optimizations only, PDCP is bypassed discard in uplink
PDCP SN size is 7bits for DRB, 5bits for SRB
The following PDCP layer functions are assumed not supported:
Retransmission of PDCP SDUs at handover for RLC AM;
For split bearers, routing and reordering;
PDCP status report.
The PDCP layer supports the following functions:
Header compression and decompression: ROHC only;
Transfer of user data;
In-sequence delivery of upper layer PDUs at PDCP re-establishment procedure for RLC AM;
Duplicate detection of lower layer SDUs at PDCP re-establishment procedure for RLC AM;
Ciphering and deciphering;
Timer-based SDU

## Slide 29: ASN.1
R2-162318 ASN.1 Structure Using Multiple Modules
R2-162493 RRC structure for NB-IOT
Figure 1: Two-module structure(R2-162318)
Separate ASN.1 structure for NB-IoT and LTE :
tags (-- ASN1START/-- ASN1STOP) for LTE
tags (-- ASN1_NB_START/-- ASN1_NB_STOP) for NB-IoT.
Some portion of the LTE IEs in EUTRA-RRC-Definitions is imported into NBIOT-RRC-Definitions.

## Slide 30
NB-IoT SIG Test Issues

## Slide 31: New Test States 1/2
The figure below shows NB-IOT UE test states which can be used in the initial condition of the test cases.
(Note: In some TCs the UE may be transferred from State 1 to State 2 directly, while in some others the UE may be transferred from State 1 to State 2 through State 2B, FFS)
State 1 Switched OFF
State 2B Registered without PDN Idle Mode
State 2 Registered Idle Mode
State 2A Registered Test Mode Activated
State 2C Registered without PDN Test Mode Activated for Data over NAS
State 3B SRB Established
State 3 Generic RB Established
State 3A Generic RB Established Test Mode Activated
State 3C SRB Established Test Mode Activated for Data over NAS
State 4 Loopback Activated
State 4A Loopback Activated for Data over NAS

## Slide 32: New Test States 2/2
 |  | RRC | ECM | EMM | ESM
State 1 | Switched OFF | ----- | ----- | ----- | -----
State 2 | Registered, Idle Mode | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | 1 default EPS bearer context active.
State 2A | Registered, Idle Mode, UE Test Mode Activated | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | 1 default EPS bearer context active.
State 2B | Registered, without PDN, Idle Mode | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | No EPS bearer context active
State 2C | Registered, without PDN,Idle Mode, UE Test Mode Activated | RRC_IDLE | ECM-IDLE | EMM-REGISTERED | No EPS bearer context active.
State 3 | Generic RB Established | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases. | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 3A | Generic RB Established, UE Test Mode Activated | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases. | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 3B | SRB Established | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active
State 3C | Loopback Activated, CP CIOT optimization only | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active.
State 4 | Loopback Activated | RRC_CONNECTED 1 + N (0 ≤ N ≤ 1) data radio bearers configured as specified in the test cases . | ECM-CONNECTED | EMM-REGISTERED | 1 default EPS bearer context active and N (0 ≤ N ≤ 1) dedicated EPS bearers active as specified in the test cases.
State 4A | Loopback Activated(for data over NAS under CP only) | RRC_CONNECTED | ECM-CONNECTED | EMM-REGISTERED | No EPS bearer context active.
Note: States in black are imported from legacy LTE, states in red are new.

## Slide 33: New Test loop function
The existing UE test loop functions for layer 2 (MAC, RLC, PDCP) and data radio bearer testing of Legacy LTE are based on DRB data’s loopback through User Plane.
It has been agreed that CP solution is mandatory for NB-IoT UE. A New UE test loop function is required in TS 36.509 and New Layer 2 test models are required in TS 36.523-3 for MAC/RLC and Data over NAS testing through Control Plane.
Affected test cases:
almost all MAC test cases, all RLC test cases and some multilayer test cases under CP solution.

## Slide 34: New AT Command
    On the UE side, since the CP CIOT optimization , UP CIOT optimization and attach without PDN are related to UE’s behavior, and CP solution is mandatory , it may be possible to add two new AT commands, one for UE initiating UP CIOT optimization negotiation and one for attach without PDN negotiation.
    On the test system side, it may be possible to specify generic procedures for bringing UE into state 2B, state 2C, state 3C, and state 4A respectively.

## Slide 35: Issues left for Clarifications
The conditions, restrictions and usages for RRC connection established with cause “mo-ExceptionData” (RAN2/CT1)
Whether resume procedure could be applied under CP solution (RAN2/SA2)

## Slide 36: Test Case Optimization Policies
Using a single TC cover several general features under normal in different layers, such as: PLMN selection, Attach/Detach, AUT, SEC, Paging, RRC Con Est/Reconf/Release…
REJECT/Abnormal TCs
Using CP solution / Single Tone as the default configurations and avoiding duplicated testing for the same functionality under other configurations (UP / Multi Tone)
RAN2 has agreed that both RRC connection Establishment and Resume are subject to Access Barring. Is the AC test cases under resume scenario need?( same situation in MFBI test cases TC 6.1.2.19, TC 6.1.2.20, TC6.1.2.21 and EAB test cases TC 8.1.2.7 and so on.)

## Slide 37: Organization of Test Specs
287 signaling testcases roughly estimated (before Testcase optimization)
12 sub clauses covers most chapters of 36.523-1
60% testcases may be co-exist with the legacy test cases, 20% testcases need modification greatly, 20% are totally new.
Proposals：
Separate all testcases in 36.523-1 within all chapters
Separate chapter for NB-IoT in 36.523-1 (36.508)
Separate TS for NB-IoT(IoT)

## Slide 38
Thanks