## Slide 1: Summary of NR progress in RAN4
CMCC
3GPP TSG-RAN WG5 Meeting #77 R5-17xxxx Reno, US, 27 Nov – 1 Dec 2017

## Slide 2
Overall Progress
The overall RAN4 discussion for NR are divided into RF and RRM, at this moment demod has not been involved. The overall completion status of sub-6GHz is roughly 70%, mmW is about 20%.
Sub-6GHz vs mmW:
  According to the time plan, RAN4 shall complete the sub-6GHz core requirements in Dec, but it seems the progress is behind the schedule. It is high likely RAN4 will not complete all the NSA core requirements by December.
  About mmW, the progress is quite slow, RAN4 has confront difficult situation in defining OTA requirements and how to test them. It is not clear when mmW requirements will be done.
Sub-6GHz TX vs RX
  TX requirement progress is better than RX requirements.
  In TX side, the power control and MPR simulation is still under discussion which will be the limitation of TX requirement definition.
  In RX side, the NSA sensitivity discussion is quite slow due to LTE and NR interference issue.
  Even all these key requirements are solved in Dec, they still need one meeting to write them done to the spec.
Notes: Reference: R4-1703469 Workplan for NR UE and BS RF

## Slide 3
Overall time plan
TR & TS
  Up to now, the agreements has been write down in the TR, but not in the TS. There is some proposal that these agreements in TR will be moved to TS without further discussion, but it is not clear when the TS will be published.
  This may affect the RAN5 January AH meeting, so it maybe necessary to inform RAN4 about this.
For RRM
  It is also targeted to complete NSA in Dec. But situation is similar to RF. Cell detection and measurement are the key requirements, they are still under discussion. Hope all can be solved in Nov meeting.
  One issue is even they complete the requirements and write done in TS, the test cases are absent, we still need to wait for several meetings.
Notes: Reference: R4-1703469 Workplan for NR UE and BS RF

## Slide 4
Sub-6GHz RF
Requirement |  | Complete?
Tx | Tx maximum output power | • Yes except for Band n79
 | MPR | • No
 | A-MPR | • No
 | PCMAX | • No
 | Minimum output power | • Yes
 | Tx OFF power | • Yes
 | ON/OFF mask | • No
 | Power control | • No
 | Frequency error | • Yes
 | EVM | • Yes
 | Carrier leakage | • Yes except for positions of carrier
 | In-band emissions | • Yes
 | Occupied BW | • Yes
 | SEM | • Yes
 | ACLR | • Yes
 | General spurious | • Yes
 | Additional spurious | • Yes
 | UE-to-UE coexistence | • No
 | Tx intermodulation | • Yes
Rx | REFSENS | • No
 | Maximum input level | • No
 | ACS | • Yes
 | In-band blocking | • Yes except for Band n79
 | Out-of-band blocking | • No
 | Narrow-band blocking | • No
 | Spurious response | • Yes
 | Rx intermodulation | • No
 | Rx spurious emission | • No
 | Receiver image | • Not for single carrier
 | [New] In-channel selectivity | • Yes
Notes: Reference: R4-1703469 Workplan for NR UE and BS RF

## Slide 5
mmW RF
Requirement |  | Complete?
Tx | Tx maximum output power | • No
 | MPR | • No
 | A-MPR | • No
 | PCMAX | • No
 | Minimum output power | • Yes (from core spec perspective)
 | Tx OFF power | • No
 | ON/OFF mask | • No
 | Power control | • No
 | Frequency error | • No
 | EVM | • No
 | Carrier leakage | • No
 | In-band emissions | • No
 | Occupied BW | • Yes
 | SEM | • Yes
 | ACLR | • Yes
 | General spurious | • No
 | Additional spurious | • No
 | UE-to-UE coexistence | • No
 | Tx intermodulation | • Not needed
 | [New] Beam correspondence | • No
Rx | REFSENS | • No
 | Maximum input level | • Yes expect for modulation order
 | ACS | • Yes
 | In-band blocking | • Yes expect for blocker offset
 | Out-of-band blocking | • No
 | Narrow-band blocking | • Not needed
 | Spurious response | • No
 | Rx intermodulation | • Not needed
 | Rx spurious emission | • No
 | Receiver image | • Not for single carrier
 | [New] In-channel selectivity | • Yes
Notes: Reference: R4-1703469 Workplan for NR UE and BS RF

## Slide 6
NSA affection to LTE RRM
Requirements |  | Standard Affection | Status
RRC IDLE state mobility |  | No DC exist at this period | Not Affect NR
RRC connected state mobility |  | Follow existing LTE requirements | Not Affect NR
RRC connection mobility control | RRC re-establishment | Pure LTE behavior | Not Affect NR
 | Random access | Defined in 36.133, not affect 38.133 | Not Affect NR
 | RRC connection release with redirection | Pure LTE behavior | Not Affect NR
Timing and Signaling | Transmit timing & Timing advance & RLM | Defined in 38.133, not affect 36.133 | Not Affect NR
Requirements |  | Standard Affection | Status
Timing and Signaling | Interruption with DC | LTE PSCell addition/release requirements as baseline | On going
Measurement | Measurement gap pattern, inter-RAT NR measurement, measurement capability | introduced in 36.133 | On going
 | Measurement accuracy, report mapping for NR reference signals | introduced in 36.133 | On going
  In NSA scenario, DC is used. Some of LTE RRM requirements are affected by NR.
Notes: R4-1706722 Expected RRM requirements for NSA in TS36.133