## Slide 1: 5G-NR RF updates from Qualcomm for preRAN5-77 5GS Conf call

## Slide 2: 38.509/38.508 impact: UE beamlock function for 5G-NR
5G-NR NSA testing in range2 may necessitate an OTA LTE anchor
  Providing a conducted LTE anchor would disturb the mmWave OTA measurement
Some of the challenges of having a OTA LTE anchor
  ensure reliability of the LTE OTA link
    Define appropriate DL power, TM mode, MCS
    No DL or UL grants after 5G-NR connection setup.
      Do we require active 5G-NR signaling over LTE link which would need LTE DL/UL Traffic?
  Impact to OTA chamber dimensions due to OTA LTE
  Impact of multipath due to reflections for OTA LTE

## Slide 3: LTE OTA considerations for NSA testing
5G-NR NSA testing in range2 may necessitate an OTA LTE anchor
  Providing a conducted LTE anchor would disturb the mmWave OTA measurement
Some of the challenges of having a OTA LTE anchor
  ensure reliability of the LTE OTA link
    Define appropriate DL power, TM mode, MCS
    No DL or UL grants after 5G-NR connection setup.
      Do we require active 5G-NR signaling over LTE link which would need LTE DL/UL Traffic?
  Impact to OTA chamber dimensions due to OTA LTE
  Impact of multipath due to reflections for OTA LTE

## Slide 4: Updates to 38.521-3 – Interworking between NR range1 & range2 and NR & LTE
There are discussions to define requirements for NR-FR 1+ NR-FR 2 and LTE +NR as two major subsections of the spec.
  LTE + NR would be further divided into LTE +NR-FR1 and LTE +NR-FR 2.
NR-FR 1 will be conducted and the requirements are available in 38.101-1 draft spec
NR-FR 2 will be OTA and the requirements are currently TBD
NR+LTE is TBD
Discussion on the Interworking requirements are expected to gather momentum in Reno with no major agreements till now.
Defining connection diagrams for NR-FR-1 & NR-FR-2 combo would be a challenge.
Tib/Rib requirements would be considered zero for all scenarios which need less than or equal to 0.5dB.
  This can compact the test spec structure and test requirements in 38.521-3.