## Slide 1: Pre RAN5#77 - 5G RRC WP Progress– NSA Focus

## Slide 2
Progress
Below are the sub-areas for Dual Connectivity for RRC
  Ch. 8.2.1: System Information Handling/ UE Capability Co-ordination
  Ch. 8.2.2: Bearer Addition, Modification and Release  Almost Done (Scope and TC Definition)
  Ch. 8.2.3: Measurements, Reporting and Handovers  Almost Done (Scope and TC Definition)
  Ch. 8.2.4: Carrier Aggregation
  Ch. 8.2.5: Reconfiguration Failure/ Radio link failure
TC Structure Options (8.2.2.1 as ex) – Consider all MR-DC options now?
Option#1 - Under each sub-areas, the test title will be generic and can be repeated for option 3, 4 & 7, for ex -
  8.2.2.1 – PScell Addition / SCG split bearer option
    8.2.2.1a - PScell Addition / SCG split bearer option for EN-DC (Option 3)
    8.2.2.1b - PScell Addition / SCG split bearer option for NGEN-DC (Option 7)
    8.2.2.1c - PScell Addition / SCG split bearer option for NE-DC (Option 4)
Option#2 – Just Focus on EN-DC for now and add option 4 and 7 in another section once 5G Core is available. For ex -
    8.2.2.1 – NR Addition / SCG split bearer option

## Slide 3
Challenges
For Bearer Addition, Modification and Release, all supported options below needs to be tested. (As per TS 37.340, these are all mandatory) -
Loopback Modes needed to verify these test cases as well, looping back data in both LTE and NR.
Multi-PDN consideration for IMS PDN on LTE
Possible cell level and beam level measurement\reporting criteria for mmW test case.
Simultaneous Bearer Combination Support | MCG only Bearer | SCG only Bearer | MCG Split Bearer | SCG Split Bearer
MCG only Bearer | Yes | Yes | Yes | Yes
SCG only Bearer | Yes | Yes | No | Yes
MCG Split Bearer | Yes | No | Yes | No
SCG Split Bearer | Yes | Yes | No | Yes

## Slide 4
Next Steps
RAN2 is making good progress for completing RRC Reconfiguration and other parts needed for NSA option 3. However, there are still changes and new agreements ongoing. Draft RRC specs (TS 38.331 and TS 36.331) for NR and LTE not updated yet.
Some scoping will continue even after Dec-17 meeting.
Possible Model Test Case can be discussed in RAN5#77 meeting to hash out more issues in implementation. Generic Procedures can be defined for initial UE state (s).
LTE RRC impact in TS 36.331 needs to be scoped out as well. This has increased the scope of test specifications. All NR related changes will be covered in TS 38.523-1 under RRC Dual Connectivity.